## Slide 1
DOE Design of Experiments Practical Training
From DOE fundamentals through full/fractional factorial and RSM; includes Minitab steps and sample data
QTank
Knowledge Code 6.4.1 · DOE Fundamentals & Advanced
qtank.org

## Slide 2
CONTENTS
Agenda
  DOE Fundamentals
  Experimental Design Types
  Essentials of Statistical Analysis Methods
  Minitab Hands-On Guide
  Industrial Case Studies
  Advanced Design and Applications

## Slide 3
Part.
01
DOE Fundamentals

## Slide 4
Definition and Scope
Designed experiments are a major branch of mathematical statistics, focused on scientifically arranging trials to optimize data collection and support valid statistical conclusions.
Core Value
By reducing runs and controlling variation sources, DOE greatly improves research efficiency in industrial optimization, pharmaceutical R&D, and more.
Goal Orientation
Clarify the problem type (e.g., factor screening, parameter optimization) and define the scope of generalization and statistical power.
Cost-Benefit Trade-off
Balance experimental cost, time, and data quality during design to avoid waste.
Structured Thinking
Require upfront planning of unit allocation, randomization, and analysis framework to ensure credible results.
Definition and Core Value of Designed Experiments
01
02
03
04
05

## Slide 5
Hypothesis-Driven
Variable Control
Execute in three phases: screening (key factors), main experiment (precise modeling), and confirmation (extrapolation).
Phased Approach
Use orthogonal arrays to ensure factor independence and assess each factor's contribution to the response.
Orthogonality Principle
Replicate runs to estimate error variance; randomize run order to eliminate systematic bias.
Replication and Randomization
Every experiment starts from a testable scientific hypothesis with clear causal or directional expectations.
Distinguish controllable factors (temperature, concentration) from noise variables (environmental fluctuation); use blocking or randomization to reduce interference.
Scientific Experimentation Framework

## Slide 6
Factor
Level
Response
Example
Optimization Direction
Controllable input variable in the experiment
Independent Variable
Specific value set for a factor
Setting
Measured output from the experiment
Dependent Variable
Levels: 100°C / 150°C / 200°C
Temperature Factor
Factor Screening
Level Optimization
Response Analysis
Factor–Level–Response Relationships
Key Elements: Factor / Level / Response

## Slide 7
Part.
02
Experimental Design Types

## Slide 8
Full Factorial Design: Principles and Applications
Full Factorial Design Definition
Factor Level Selection
Advantages of Full Factorial Design
Full factorial design includes all possible factor level combinations to comprehensively explore each factor's effect on the response.
Full factorial design accurately estimates each factor and interaction, avoids missing important effects, and improves reliability and precision.
Choose factor level counts balancing comprehensiveness against cost and time—typically two- or three-level designs.
Replication and Randomization in Experiments
Full Factorial Design Applications
Replication and randomization in full factorial designs improve stability, reduce error, and ensure reliable results.
Full factorial design is widely used in product development, process optimization, and quality control when comprehensive factor understanding is required.
Full Factorial Data Analysis
Full factorial data analysis typically uses ANOVA, comparing response means across level combinations to reveal factor and interaction effects.

## Slide 9
Fractional Factorial Implementation Strategies
Use resolution IV or V designs (e.g., 2^(k−p)) so main effects are not aliased with two-way interactions—prioritize clear main effects in screening.
Alias Structure Management
Foldover (e.g., reversing generator signs) on an initial fractional design separates aliased interactions—useful in confirmation phases.
Foldover Design to Increase Resolution
High-quality fractional designs project to full factorials on important subsets—e.g., a 7-factor 1/8 design remains full on any 3 factors.
Projection Property Applications
When standard tables don't apply, use intelligent algorithms for custom designs—especially mixed-level or heavily constrained scenarios.
Genetic Algorithm Optimization
Use Plackett-Burman and similar constructions to screen many factors with few runs (e.g., 12 runs for 11 factors).
Minimize Experimental Runs

## Slide 10
01
02
04
03
05
06
Form the Team
Identify Factors
Analyze Current State
Screen key input variables and their interactions on the output.
Evaluate Responses
Adjust Parameters
Iterative Optimization
Design the Experiment
Run the Experiment
Build the Model
Identify Factors
Build a second-order polynomial model to describe nonlinear relationships between variables and responses.
Modeling & Analysis
Use CCD or BBD to determine the spatial distribution of experimental points.
Design the Plan
Allocate equipment, personnel, materials, and other resources per the experimental plan.
Allocate Resources
Execute experiments per the design matrix and record response data.
Run Experiments
Confirm model validity through residual analysis and goodness-of-fit tests.
Model Validation
Optimization Steps
Verify Results
Response Surface Method Optimization Path

## Slide 11
Part.
03
Essentials of Statistical Analysis Methods

## Slide 12
Analysis of Variance (ANOVA) Principles
The core idea of ANOVA is to partition total variation into between-group and within-group components. The F ratio (between-group variance / within-group variance) tests whether treatment effects are significant. Between-group variation reflects differences across treatment levels; within-group variation reflects random error.
01
ANOVA requires data to meet normality assumptions, typically verified by Shapiro-Wilk test or Q-Q plots. If data deviate severely from normality, use nonparametric tests (e.g., Kruskal-Wallis) or transformations (e.g., log transform).
02
Homogeneity of Variance Test
Group variances must be homogeneous (homoscedasticity), assessed by Levene or Bartlett tests. If variances are unequal, use Welch-corrected ANOVA or Games-Howell post-hoc comparisons.
03
When the overall test is significant, perform post-hoc multiple comparisons (e.g., Tukey HSD, Bonferroni correction) to control family-wise error rate (FWER). Modern methods such as Holm-Bonferroni step-down improve test power.
04
Beyond p-values, report effect sizes such as η² (eta-squared) or ω² (omega-squared) to quantify the proportion of variance explained by treatments. η² > 0.14 is typically considered a large effect.
05
Normality Assumption Requirements
Effect Size Calculation
Multiple Comparison Control
Variance Decomposition Principle

## Slide 13
Main Effects
Interactions
Case Analysis
Interpreting Main Effects and Interactions
Effect Analysis
Use variance decomposition to identify main effects of each factor—e.g., the independent impact of temperature and pressure on yield. Example: temperature main effect p < 0.05 indicates a significant factor.
Interaction Plots
Display two-factor interaction plots to illustrate nonlinear effect combinations. Example: when temperature × pressure interaction is significant, use contour plots.
Effect Comparison
Compare effect sizes to identify key factors—e.g., temperature effect size 0.8 far exceeds pressure 0.3. Example: ANOVA shows Factor A contributes over 60%.
01
02
03

## Slide 14
Completely Randomized Design
Stratified Randomization
Key Points for Randomization
Covariate Adjustment
Randomized Block Design
Randomization and Blocking Techniques
For homogeneous experimental units, assign treatments completely at random via random number tables or software so each unit has equal chance of any treatment, controlling unknown confounders.
When heterogeneity is evident (e.g., site or batch differences), group similar units into blocks and randomize treatments within blocks. Common types include RCBD and Latin square designs.
For continuous confounders not controlled by randomization (e.g., baseline measurements), use ANCOVA to adjust statistically and improve treatment effect estimates.
In multi-center clinical trials, stratify randomization by center to balance treatment groups within each site. Predefine stratification factors and ensure adequate sample size per stratum.
Use sealed envelopes or central randomization (IWRS) for allocation concealment to prevent selection bias. Document randomization sequence generation for audit.

## Slide 15
Part.
04
Minitab Hands-On Guide

## Slide 16
Full Factorial Design Steps
Create the Experimental Design
In Minitab, select Stat > DOE > Factorial > Create Factorial Design; enter factor count and levels, set center points and replicates, and generate the full factorial run table.
Data Entry and Coding
Enter experimental data in the Minitab worksheet with correct factor coding (typically −1 = low level, +1 = high level) for analysis and visualization.
Model Fitting and ANOVA
Fit the model via Stat > DOE > Factorial > Analyze Factorial Design; check main and interaction significance and use the ANOVA table to assess overall model validity.
Residual Diagnostics and Model Validation
Use Graph to generate residual plots (normal probability, residuals vs. fitted, etc.) to verify assumptions and detect outliers or nonlinear trends.
Optimization and Prediction
Use the Response Optimizer to set response goals (maximize, minimize, or target), generate optimal parameter combinations and predictions, and save the plan for production.

## Slide 17
Fractional Factorial Design Workflow
In Minitab, select Stat > DOE > Factorial > Create Factorial Design, check "Fractional factorial," and choose resolution (e.g., IV or V) to balance efficiency against aliasing risk.
Design Generation and Resolution Selection
Use "Display Aliases" to review confounding; prioritize clear main effects and two-way interactions, adjusting generators or adding runs when needed.
Alias Structure Analysis
Generate main effects, interaction, and contour plots to identify sensitive regions and guide factor adjustment decisions.
Reading Effect and Contour Plots
If significant effects are aliased, add foldover runs via "Fold Design" to de-alias and strengthen conclusions.
Foldover Design for Confirmation
After entering data, use stepwise regression or manually drop nonsignificant terms (p > 0.1) to simplify the model while retaining significant effects.
Data Collection and Model Reduction

## Slide 18
Systematically resolve key surface-modeling issues to ensure reliable response optimization
Issue 01: Inadequate Model Fit
Second-order model fails to fit adequately; significant lack-of-fit is present
Increase center-point replicates to estimate pure error and test lack of fit
1
Apply Box-Cox transformation for non-normal response data
2
Issue 03: Multiple Response Optimization
Multiple responses conflict; difficult to optimize all simultaneously
Build desirability functions for multi-objective optimization
1
Use Minitab Response Optimizer to find the Pareto frontier
2
Issue 02: Inappropriate Factor Ranges
Factor levels set outside the feasible region, causing distorted predictions
Use steepest ascent to define reasonable factor ranges
1
Validate the operating window with Minitab contour plots
2
Issue 04: Misidentifying Surface Features
Saddle points or ridge systems mistaken for extrema
Confirm surface type via eigenvalue analysis
1
Add axial runs to verify curvature direction
2
Response Surface Analysis Execution
Improvement Strategy: Range Adjustment
Improvement Strategy: Feature Verification
Improvement Strategy: Model Optimization
Improvement Strategy: Weight Allocation

## Slide 19
Part.
05
Industrial Case Studies

## Slide 20
Microwave Popcorn Parameter Optimization
Based on package size and target pop rate, use DOE to find optimal heating power—avoiding scorching from excess power or unpopped kernels from insufficient power.
Heating Power Selection
Heating Time Control
Microwave Frequency Adjustment
Packaging Material Microwave Transparency
Initial Moisture Content
Vent Hole Design Optimization
Run time-gradient experiments combining expansion ratio and taste scores to find the heating-time sweet spot balancing efficiency and quality.
Optimize microwave frequency via orthogonal experiments to account for batch dielectric differences and ensure uniform energy absorption.
Test packaging materials for microwave transparency and pop uniformity to select the optimal material combination.
Control preprocessing to set moisture levels and build quantitative models linking moisture to pop rate and hardness.
Compare vent count, diameter, and placement via pressure monitoring and yield statistics to determine optimal vent geometry.

## Slide 21
Dynamic Laser Power Adjustment
Workpiece Preheat Temperature Control
Robot Path Planning
Wire Feed Speed Calibration
Shielding Gas Mix Ratio Experiment
Welding Process Parameter Improvement
Using real-time weld imaging feedback, build a power gradient model (800–1500 W stepwise control), reducing porosity from 3.2% to below 0.5%.
Optimize Ar/CO₂ mix (75/25 to 85/15) via RSM to reduce spatter and improve penetration consistency.
Apply Six Sigma to control wire feed variation (±0.3 m/min), stabilizing Mn/Si ratio in deposited metal at 2.1–2.3.
Develop stepped preheat (80°C → 120°C → 150°C) for high-strength steel welding, reducing cold-crack risk to < 0.1% incidence.
Use genetic algorithms to optimize torch path, cutting non-arc time to under 12% of total cycle time.

## Slide 22
Apply DOE to production data to identify key factors and their interactions
Factor Analysis
Validate optimization stability and reliability through replicate runs
Verify Results
Use full or fractional factorial designs to model process parameters vs. quality characteristics
Experimental Design
Establish SPC control charts to monitor key process parameters
Implement Monitoring
Determine optimal process parameter combinations via RSM
Parameter Optimization
Compare Cpk improvement before and after optimization
Effectiveness Evaluation
Data Collection
Process Parameter Optimization
Identify key process parameters using DOE
Manufacturing Process Capability Enhancement
Plan Generation

## Slide 23
Part.
06
Advanced Design and Applications

## Slide 24
Model Building
Build second-order polynomial models via central composite design to capture interactions and nonlinear response features.
01
Robust Design
Introduce noise factors for robustness optimization; balance mean and variance via dual-response surfaces to improve process robustness.
03
Parameter Tuning
Use steepest ascent for optimization direction; adjust factor levels with confidence intervals for precise response control.
02
Surface Analysis
Use contour and 3D response surface plots to locate extrema, optimal regions, and sensitive factor ranges.
04
Confirmation Runs
Confirm optimization via replicate runs and prediction intervals to close the optimization loop.
06
Multi-Objective Optimization
Integrate multiple responses via desirability functions and Pareto frontiers for multi-objective decisions.
05
Deep RSM optimization for globally optimal process parameters
Advanced Response Surface Optimization

## Slide 25
Convert mean-and-variance dual objectives to a single robustness metric via S/N ratio—highly effective in automotive tolerance design.
Taguchi Method Core Principles
Use quality loss functions to quantify variation cost and guide optimal tolerance decisions in medical device R&D.
Deliberately simulate temperature/humidity variation in consumer electronics testing to identify sensitive design parameters early.
01
03
02
Robust Design to Reduce Variation
For photoelectric sensor response issues, model signal–noise factor interactions to improve environmental adaptability.
A three-tier verification system—simulation, bench test, field test—ensures design reliability.
04
05
Dynamic Characteristic Optimization
Active Introduction of Noise Factors
Multi-Stage Robustness Verification
Economic Balance in Tolerance Design

## Slide 26
Balancing Multiple Response Variables
Integrated Desirability Function Approach
Pareto Frontier Applications
Constrained Optimization Modeling Techniques
PCA Dimensionality Reduction
Cost Weight Allocation Model
Convert multiple responses to 0–1 desirability indices to resolve dimensional accuracy vs. surface finish conflicts in injection molding.
Use NSGA-II to generate non-dominated solution sets for multi-dimensional aerospace material selection.
Apply Lagrange multipliers for hard constraints between responses, balancing energy density and safety in cathode material development.
Cluster 20+ quality characteristics to simplify rubber formulation optimization.
Use QFD house of quality to translate customer needs into technical weights for multi-objective appliance parameter decisions.

## Slide 27
Thank You
qtank.org
QTank
qtank.org