## Slide 1
QC Inspection Practical Training
Incoming, In-Process, & Final Product Inspection Standards
New Employee Training: IQC / IPQC / FQC / OQC Inspection System & Abnormality Loop Closure
QTank
Knowledge Code 11.1.1 · IQC/IPQC/FQC/OQC Planning
qtank.org

## Slide 2
What We'll Cover
Four sections: From system map to completing a qualified inspection
Training Roadmap
From Standards
To Judgments
No theory, just practical actions: Which standards, what tools, how to sample, judge, & handle abnormalities
4 Chaps
18 Pgs
01
Inspection Overview & Prep for New Roles
Understand the role of the Three-Inspection system, learn internal calibration, record keeping, & prep before starting
02
Incoming Inspection IQC
Learn sampling plans, box verification, visual inspection, & use of Four-Color labels to block defects
03
In-Process Inspection IPQC
Master first piece confirmation, fixed route patrol, & use Cpk to assess process stability
04
Final Product Inspection & Abnormality Loop Closure
Understand glass inspection items, judgment criteria, & Four-Step abnormality closure before shipment
QC Inspection Practical Training · Quality Department
02 / 18

## Slide 3
CHAPTER 01
01
Inspection Overview
Preparation for Onboarding
QC Inspection Practical Training
What This Chapter Addresses
On the first day, what should I understand first?
The 3-Inspection System blocks defects at each stage. Understanding standards, gauges, & records is crucial for accurate judgments.
3-Inspection System
Gauge Calibration
Inspection Records
03 / 18

## Slide 4
3-Inspection System: Where Defects Are Blocked
IQC / IPQC / FQC / OQC: What Each Stops & Why Early Stopping Is Cheaper
A glass panel must pass 4 stages. Each stage has different responsibilities, but the goal is the same: No defects move on.
Earlier Stopping, Cheaper
Blocked at IQC
≈ $1
Blocked at IPQC
≈ $10
Reaches Customer
≥ $100
1-10-100 rule: The later a defective glass is found, the higher the cost. Numbers are industry standards.
IQC
Incoming inspection · stopped at the factory gate
Raw glass, targets, cleaning agents, packaging materials; only qualified items allowed in stock.
IPQC
Process Inspect. · Block Before Batch
First-piece confirm, periodic checks, key param. & appearance monitoring; stop issues on-site.
FQC
Final Inspect. · Block Before Stock
Final appearance & optical eval. before stock; decide if qualified for storage.
OQC
Outgoing Inspect. · Block Before Customer
Verify qty & packaging labels per shipping order; release after spot check.
Any NG: mark, isolate, report immediately—never pass down.
QC Inspection Practical Training · Quality Department
04 / 18

## Slide 5
Three Essentials: Std, Gauges, Records
Prepare these three before starting; don't inspect without all.
01
Std
Check std first, then inspect. The Inspection Std, Sampling Std, & Limit Sample are the only basis; judging by feel is a major new hire issue.
First task: confirm std is current & controlled.
02
Gauges
Calipers, feeler gauges, and micrometers must be within their valid calibration period, with appropriate range and accuracy. They should be zeroed before use and stored by designated personnel. Any measurement results obtained with expired gauges are invalid.
Check cal. tag before using; return expired gauges to metrology lab.
03
Records
Record on-site, legibly; correct errors with a line and sign; no blacking out, no backdating. Data is the sole evidence for eval. & traceability.
Cross out wrong numbers, write correct value & sign.
QC Inspection Practical Training · Quality Department
05 / 18

## Slide 6
Internal gauge cal.: Ensure every gauge is reliable
Self-calibrate, on schedule, keep records — any gauge inaccuracy invalidates all insp. results
01
Log
Assign unique codes to each gauge, register model, range, storage location & responsible person
Re-register after addition or repair
02
Schedule
Set calibration cycle based on type & usage, remind before expiration, no "use for now"
Cycle set by metrology admin, no extension allowed
03
Select Std. Ref.
Calibrate with gauge blocks, std. sheets; ref. precision must exceed gauge, and be traceable
Std. refs. also need periodic external calibration
04
Calibrate
Calibrate at zero, mid, & full range; record actual deviation & compare with allowed error
Deviation exceeds limits: Adjust first, NG then stop
05
Label & Trace
Post calibration label, fill out the internal calibration record form, state conclusion & calibrator
Label must be on the gauge itself, not just the box
Internal calibration = in-house calibration: use traceable std. refs. to verify gauges on schedule, ensuring they are within allowed error
Gauge Calibration Labels: Three States
Pass
Valid within period, use for insp.
Restricted Use
For specified range or inspection items only
Out of Service
Expired, damaged, or out of tolerance; send to metrology room
Label on gauge, not material. Must include: gauge code / cal date / expiry / cal person's signature. Missing any = out of service
Daily Checks: Three Steps
Before Use
Check cal label, close calipers to verify zero
During Use
Select points within range, avoid over-range, tapping, or high-temp parts
After Use
Clean & return, prevent rust on metal gauges; stop use & send to metrology if issues
Judgments made with expired gauges are invalid; re-inspect required
QC Inspection Practical Training · Quality Department
06 / 18

## Slide 7
Inspection Records: How to Fill
Records are for your judgment & traceability, not just for inspection
Record Fields | What to Write | Common Errors
Batch & Material Code | Supplier batch + internal code; both required | Only write part no., can't trace incoming batch if issues arise
Inspection Time | Year / Month / Day + Shift, precise to specific time | Only write date, can't identify which shift
Sampling & Meas. | Sample size n, defect count d, key item meas. values | Only write 'Pass', no data, can't verify
Judgment Basis | Cite version & clause no. of Inspection Standard Book | Conclusion doesn't match standard clause, can't prove
Inspector | Handwrite signature & clear inspection date | No proxy signing, no stamp instead of signature
Fields vary by form (incoming, in-process, final, NCR), but these five are essential—missing any makes the record non-traceable
Four No-Fill Rules
No Altering
Cross out errors, write correct value & sign
No Backdating
Record on-site, backdated entries are invalid
No Blank Fields
If no content, fill with '/'; no blanks allowed
No proxy signing
Must sign personally; no stamps or proxies
How to use records: two traceability chains
Forward
Batch No. → Inspect. Record → Decision → Release?
Reverse
Customer complaint → Batch No. → Inspect. Record → Measuring tools & process params
Record retention & destruction follow company's Record Control Procedure; no unauthorized lending, altering, or destruction
QC Inspection Practical Training · Quality Department
07 / 18

## Slide 8
CHAPTER 02
02
Incoming Inspect.
IQC
QC Inspection Practical Training
What This Chapter Addresses
How to sample, judge, & release incoming materials?
IQC's role is to block nonconformities at the gate—sampling plan, box check, color coding, no steps skipped. Skipping any step will cost 10x later.
Sampling Plan
Box Check
Color Coding
08 / 18

## Slide 9
How to sample: batch size determines sample size
Turn 'how many to sample, how many to judge' into a rule anyone can follow
Incoming batch N (pcs) | Sample size n | Acceptance number Ac | Reject Num Re
91 – 150 | 20 | 0 | 1
501 – 1,200 | 80 | 2 | 3
3,201 – 10,000 | 200 | 5 | 6
Example based on GB/T 2828.1 (counting sampling insp. proc.) general insp. level II, AQL 1.0. For teaching only; actual exec. follows company's 'Sampling Std.' & product 'Inspection Std. Book'.
Sampling Principles
Random
Equal chance for each box, pallet; no fixed position
Stratified
Cover different pallets, batches, top & bottom layers
No Selection
No bias for good or bad
How to judge after getting the numbers
d ≤ Ac
Batch passes, green label, release to warehouse
d ≥ Re
Batch fails, reject & report immediately
d = defect num in sample; no intermediate state between Ac & Re (Re = Ac + 1)
QC Inspection Practical Training · Quality Department
09 / 18

## Slide 10
IQC Practical: Four-Step Judgement & Four-Color Labels
Check before opening, inspect first after opening—follow to avoid missing steps
Four-Step Method
01
Verify
Delivery note, part no., batch, prod. date, COA & packaging integrity; stop if any missing
02
Visual
Illuminance > 1000lx, back & side lighting; wear clean gloves, no bare hands on film
03
Performance
Sample key optical & size items per the Inspection Standard Book, record actual values.
04
Labeling
Label immediately after judgment, store in designated areas, & enter into system. No delays.
Pass
Nonconforming
Pending Judgment
Concession Acceptance
Uninspected materials must not be used.
QC Inspection Practical Training · Quality Department
10 / 18

## Slide 11
CHAPTER 03
03
Process Inspection
IPQC
QC Inspection Practical Training
What This Chapter Addresses
Who stops the process before batch rejection?
IPQC's role is to intercept before batch defects—1st piece check, timed patrols, & process capability monitoring. Early action minimizes loss.
1st Piece Check
Patrol Route
Process Capability
11 / 18

## Slide 12
1st piece check: 1st gate after startup
Change type, material, mold, adjustment, or long downtime—1st piece required in all cases.
1st Piece Required
Change Type
Change Material
Change Mold
Equipment Adjustment
Machine Downtime
Refer to the plant's 'First Piece Confirmation Mgmt.' for specific triggers & downtime limits.
10 mins saved on first piece avoids hours of batch scrap.
What Constitutes Compliance
1st piece at startup + 3 consecutive pieces after stabilization; check appearance, key dimensions, optical metrics, compare with limits, record process params, sign off before batch production.
First Piece Nonconformance
Stop immediately, isolate produced items, notify process to investigate, confirm fix before restarting; no "just try" production.
QC Inspection Practical Training · Quality Department
12 / 18

## Slide 13
Inspection: 5 Must-Checks & Anomaly Reporting
Fixed freq., fixed route, fixed records reveal changes.
Inspection isn't just a formality. All changes between inspections are detected by fixed actions—fixed freq., route, & record method.
Inspection Freq. & Route
Every 2 hours
Or set by N pieces / pallet. Freq. determined by process risk, not workload.
Fixed route by process order: no backtracking, no skipping; check & sign each item on the inspection sheet, record anomalies with time, machine, batch, & details.
People
Following SOP, wearing dust cap, gloves, & work uniform
Machine
Params within range, no alarms or unusual sounds
Material
Check if the in-process product status labels are correct, and ensure there is no mixing of conforming and non-conforming items.
Method
Verify if work instructions are the latest controlled version
Env.
Check if cleanliness, temp., humidity, & lighting are within specs.
Detect anomaly → Notify team leader / process eng. → Hang "Pending" sign → Trace all products since last OK inspection.
QC Inspection Practical Training · Quality Department
13 / 18

## Slide 14
Cpk > 1.33 for process control
Yield is post-facto, Cpk is proactive — don't let high yields mask drifting processes
Process capability threshold
Cpk ≥
1.33
Basic threshold for process control
The pass rate is a "post-event" result, while Cpk is a "pre-event" warning. Even if a batch is entirely qualified, the process may be quietly drifting towards the specification limits—relying solely on the pass rate would completely mask this risk.
3 steps when Cpk is low:
① Check centering → Adjust machine ② Check variation → Change material / maintain ③ Verify
Cp · Precision only
Spec. width ÷ 6σ, no centering considered
Cpk · Centering & precision
Considers centering; takes the worse side
Two common rules for control charts: 7 consecutive points on one side of center line, 7 consecutive points rising or falling — report immediately if any occur.
QC Inspection Practical Training · Quality Department
14 / 18

## Slide 15
CHAPTER 04
04
Final product inspection
Anomaly closure
QC Inspection Practical Training
What This Chapter Addresses
What to confirm before release?
Shipping release is the final commitment to the client—glass inspection, criteria, and four-step closure. Sign off, and take responsibility for the box.
Glass Spec.
Judgment Basis
4-Step Closure
15 / 18

## Slide 16
FQC / OQC: What to inspect, criteria
Five inspection items, five methods, five standards—always cite a source
Inspection Items | Inspection Methods | Judgment Basis
Visual defects: Scratches / pinholes / contamination / chipping / color diff. | Bright & Backlight Visual, Limit Sample Comparison | Visual Inspection Std.
Warp & Flatness | Feel Gauge, Warp Meter, Platform Measurement | Dimensional Inspection Std.
Wavefront Distortion / Trans Reflectance | Laser Interferometer, Spectrophotometer | Optical Performance Std.
Surface Roughness / Film Thickness | White Light Interferometer, Ellipsometer | Film Layer Inspection Std.
Packaging & Labeling | Visually check shipping doc, labels, & qty | Packaging Work Standards
OQC Final Three Checks Before Release
01
Qty, box no., & shipping doc must match
02
Labels & batch info traceable to machine & prod. date
03
All spot-check items must pass, no unresolved issues
Final FQC insp. is not a second look but a final commitment to the customer. Each box released represents the company's signature.
This page lists only items & methods, not specific limits; all numerical limits follow the latest controlled version of the Inspection Standard.
QC Inspection Practical Training · Quality Department
16 / 18

## Slide 17
Nonconforming Product Handling: Four-Step Loop
The value of one anomaly lies not in 'fixing it' but in 'never happening again'
01
Labeling
Immediately label red, noting defects & qty
02
Isolate
Move to nonconforming area, no mixing with conforming
03
Review
MRB Review: Rework / Repair / Concession / Scrap
04
Dispose
Follow review conclusions, record, & close case
Three elements for traceability: batch no. + prod. date + machine no. — missing one means impact scope cannot be defined.
Loop beyond four steps: Four more actions after disposal
Find Root Cause
Ask Why 5 times to find the root cause; 'employee carelessness' is not a root cause
Set Actions
Develop corrective actions for root cause, assign responsible person & completion time
Verify Results
3 consecutive batches or no recurrence in 1 month is considered effective
Standardize
Update conclusions in SOP, inspection standards & limit samples
Two Red Lines
① Mixing non-conforming & conforming products
Isolation area must have clear physical boundaries & labels, not just mental notes
② Allowing product to flow without labels
No label means unknown status; unknown status means no traceability or release
Any violation is treated as a major quality issue, no exceptions
QC Inspection Practical Training · Quality Department
17 / 18

## Slide 18
Thank You
qtank.org
QTank
qtank.org