## Slide 1
Control Plan (CP)
Authoring and Deployment — Practical Training
Last Mile from PFMEA to Shop Floor · APQP / IATF 16949
QTank
Knowledge Code 8.3.2 · Control Plan (CP)
qtank.org

## Slide 2
Training Objectives
After training, answer: What to control? How? What if out of control?
Understand CP role in APQP / IATF 16949 and three-phase differences
Master CP standard columns and PFMEA→CP mapping rules
Write executable detection frequency, control methods, and reaction plans
Build version linkage awareness among CP, SOP, inspection specs, ECN
Verify CP is executed on shop floor via Layered Audit
Control Plan (CP) — Practical Training

## Slide 3
01
Opening Case
High PFMEA Scores, Audit Still Issues Major NC

## Slide 4
Case: Tier 1 Seat Supplier Post-PPAP Second-Party Audit
❌ Audit Findings
• CP says "sample 5 per lot"; PFMEA requires 100% torque recording • CP cites inspection spec Rev.B; shop floor uses Rev.C • Reaction plan only "notify team leader" — no stop/containment • KCC not marked; noncompliant with customer CSR
✅ Root Cause Review
• PFMEA by project engineer; CP copied from old product • Process changed three times; CP not updated via ECN • CP is the "contract for risk control on the shop floor" • Must be maintained in sync with PFMEA and SOP
Control Plan (CP) — Practical Training

## Slide 5
02
What Is a Control Plan?
CP ≠ Simple Duplicate of SOP

## Slide 6
CP Definition and APQP Position
Control Plan: what to control, which methods, which specs, how to react
SOP teaches "how to do one step"; CP summarizes "how to stay in control" from characteristics and risk
Flow chain: design intent → DFMEA → PFMEA → Control Plan → SOP → inspection spec → PPAP
Required in PPAP package; missing CP = incomplete PPAP
Control Plan (CP) — Practical Training

## Slide 7
Three-Phase Control Plan
Phase | English | Purpose
Prototype | Prototype | Validate concept; coarse controls
Pre-Production | Pre-launch | Trial verification; near production
Production | Production | Authoritative production version (audits use production CP)
Control Plan (CP) — Practical Training

## Slide 8
03
CP Standard Structure
AIAG Core Columns

## Slide 9
Typical CP Columns (Excerpt)
① Part/process number ② Process name/operation description ③ Machine, device, fixture, tooling
④ Characteristic number ⑤ Product characteristics (and tolerances) ⑥ Process characteristics (and tolerances)
⑦ Special characteristic classification (KCC/KPC per customer symbols)
⑧ Product/process specification/tolerance ⑨ Evaluation/measurement technique
⑩ Sample size/frequency ⑪ Control method ⑫ Reaction plan
OEM template column names may differ slightly; logic is consistent
Control Plan (CP) — Practical Training

## Slide 10
04
PFMEA → CP Mapping
AP=H items must have executable controls

## Slide 11
Field Mapping Overview
PFMEA Output | CP Column
Process Step | Process Name / Number
Function / Requirement | Product / Process Characteristics
Special Characteristics | Special Characteristic Symbol Column
Preventive Controls | Control Method (mistake-proofing, SOP parameters)
Detection Controls | Evaluation/Measurement + Sample/Frequency
High Severity S | Tighten frequency, 100% inspection
Optimization Actions | Update control methods and reaction plan
Control Plan (CP) — Practical Training

## Slide 12
05
Walkthrough Cases
Tightening & Injection Molding

## Slide 13
Case 1: OP40 Seat Rail M8 Tightening
PFMEA Summary
FM: Insufficient torque | FE: Seat loose S=8 FC: Torque gun out of calibration, missed tightening O=4 Prevention: daily check + missed-tightening sensor Detection: 100% torque + angle curve recording
One CP Row (Correct Format)
Product characteristic: 35±3 N·m (KCC) Process characteristic: tightening angle 540°±10° Measurement: electric torque gun + curve storage Frequency: 100% | auto line stop on exceedance Reaction: line stop → containment → engineering confirmation → restart
Control Plan (CP) — Practical Training

## Slide 14
Case 2: OP20 Injection Molding
Process Characteristic Control
Melt temp 280±5°C, hold pressure 85±5 MPa Control: X̄-R chart, n=5 subgroup per shift (Process parameters affecting dimensions)
Product Characteristic Control
Critical bore 12.0±0.1 mm First 3 pieces 100% + sample 5 every 2h Reaction: SPC out of control → stop line, adjust → 100% bore check
Control Plan (CP) — Practical Training

## Slide 15
06
Reaction Plan
Do not write "notify team leader" only

## Slide 16
Six Reaction Plan Elements (Actionable, Auditable)
① Stop
② Contain
③ Notify
④ Disposition
⑤ Verify
⑥ Record
Control Plan (CP) — Practical Training

## Slide 17
Reaction Plan Writing Essentials
Stop: line stop / lot hold / tag — clear triggers (out of spec, SPC out of control, etc.)
Contain: physical area, tag color, system lot lock
Notify: team leader / engineer / quality — roles and escalation path
Disposition: sort, scrap, rework; concession via exception process (3.4.3)
Verify: what data proves safe to resume? Who signs?
If CSR requires customer notification, include in reaction plan triggers
Control Plan (CP) — Practical Training

## Slide 18
07
Eight Steps to Author and Maintain
From Final PFMEA to Layered Audit

## Slide 19
CP Authoring and Maintenance Flow
Final PFMEA
Flow diagram + characteristics
Fill CP per operation
Compare with SOP
Trial production verification
PPAP approval
Layered audit
4M change review
Control Plan (CP) — Practical Training

## Slide 20
Layered Audit Spot-Check List
Check Item | Acceptance Criteria
CP Version | Shop-floor SOP references same revision
Special Characteristics | Drawing, CP, fixtures show KCC symbols
Frequency | Actual inspection matches CP
Records | Torque/SPC records traceable to lot
Reaction | Last out-of-control event has full reaction plan execution record
Control Plan (CP) — Practical Training

## Slide 21
08
Special Characteristics & Changes
KCC Transfer Chain and ECN

## Slide 22
Special Characteristic (KCC/KPC) Transfer
Customer drawing CC/SC → DFMEA S≥8 → PFMEA special char column → CP classification column
KCC rows on CP: frequency not weaker than PFMEA detection recommendation
Audit frequent question: "PFMEA marks SC, why no SC on CP?" → major NC
4M change, PFMEA optimization, CSR update, failed MSA → must trigger CP review
Minimum ECN package: PFMEA diff + CP diff highlight + SOP/inspection spec revision + training record
Control Plan (CP) — Practical Training

## Slide 23
CP Interface with SPC / MSA
MSA Prerequisite
Gauges in evaluation/measurement column must pass GR&R Otherwise audit asks: "Is the data credible?"
SPC Example
Melt pressure: X̄-R, n=5, one subgroup every 2h Two consecutive points beyond 2σ → team leader confirmation Any point out of spec → line stop (document in reaction plan)
Control Plan (CP) — Practical Training

## Slide 24
09
Common Pitfalls
Pitfall Avoidance Checklist

## Slide 25
Common Pitfalls and Countermeasures
Pitfall | Consequence / Countermeasure
Copy CP from old product | Missing characteristics → rebuild per PFMEA operation by operation
PFMEA updated, CP not updated | Major NC → ECN linkage
Vague reaction plan | Escalation on out-of-control → complete six elements
Product characteristics only, no process characteristics | No SPC basis → add process characteristic rows
CP and SOP on different revisions | Operators confused → three-way alignment
Control Plan (CP) — Practical Training

## Slide 26
Implementation Checklist (Excerpt)
Authoring: current PFMEA signed; operation numbers match flow diagram; KCC vs drawing checked
Authoring: each row reaction plan includes stop/contain/notify/verify/record
Trial: execute per CP frequency ≥3 lots; one simulated out-of-control drill
Production: monthly Layered Audit; CP review within 48h of 4M change
Before audit: prepare CP / PFMEA / SOP three-way comparison
Control Plan (CP) — Practical Training

## Slide 27
CP Three Questions — Every Row Must Answer
🎯
What to control?
🔧
How to control?
🚨
What if out of control?
Summary
Control Plan is proof PFMEA lives on the shop floor — quality is not page count but whether out-of-control events follow the CP. Recommendation: one line, 2 weeks PFMEA→CP→SOP alignment pilot, then roll out plant-wide.
QTank · Thank you for learning

## Slide 28
Q & A
Related article: Control Plan (CP) Authoring and Deployment · Knowledge Code 8.3.2

## Slide 29
Thank You
qtank.org
QTank
qtank.org