## Slide 1
PFMEA Seven-Step Method
Linked with Control Plan — Practical Training
AIAG-VDA Process FMEA · Making Risk Analysis Live on the Shop Floor
QTank
Knowledge Code 8.3.1 · PFMEA
qtank.org

## Slide 2
Training Objectives
After training, you should answer: Were risks identified? Are actions on the CP? Are changes updated?
Understand PFMEA role in APQP / IATF 16949 and common failure root causes
Master AIAG-VDA seven-step outputs and cross-functional responsibilities
Build FM→FE→FC failure chains and rate S/O/D with AP priority
Distinguish prevention vs detection and map high-risk items to Control Plan (CP)
Establish Living PFMEA triggers and 4M change review
PFMEA Seven-Step Method — Practical Training

## Slide 3
01
Why PFMEA Often "Fails"
Forms exist, risks remain

## Slide 4
Case: Machining Section Second-Party Audit
❌ Audit Findings
• Top 3 RPN items with no matching detection/prevention on CP • Shop-floor SOP inconsistent with PFMEA recommendations • PFMEA Rev. 2019; model changed in 2024, not updated • AP=H items without owner or completion date
✅ Value Chain
Identify process risks → select control methods → document in CP/SOP → execute on shop floor → update with 4M changes PFMEA is not an Excel trick — it is structured thinking
PFMEA Seven-Step Method — Practical Training

## Slide 5
02
Seven-Step Overview
AIAG-VDA 7-Step Approach

## Slide 6
PFMEA Seven-Step Method
Step | Name | Key Output
1 | Planning and Preparation | Scope, team, boundary diagram, historical issues
2 | Structure Analysis | Process steps, 4M elements, process items
3 | Function Analysis | Functions and requirements per step
4 | Failure Analysis | Failure Mode FM, Effect FE, Cause FC
5 | Risk Analysis | S/O/D rating, AP action priority
6 | Optimization | Prevention/detection actions, owner, target date
7 | Results Documentation | PFMEA report, links to CP/work instructions
PFMEA Seven-Step Method — Practical Training

## Slide 7
Steps 1–2: Planning, Structure
Planning: define PFMEA boundaries (from/to operation), cross-functional team, customer/regulatory inputs
Historical issues: warranty, complaints, scrap, repeat defects — prioritize in failure analysis
Structure: process steps as backbone (not legacy scattered tables per operation)
4M linkage: Man, Machine, Material, Method (Environment optional) attached to each step
Boundary diagram: clear supplier/customer process interfaces; avoid scope gaps
PFMEA Seven-Step Method — Practical Training

## Slide 8
03
Failure Chain Walkthrough
Tightening Operation FM→FE→FC

## Slide 9
Case: OP40 Bolt Tightening
Failure Chain
Function: M8 bolt torque within spec FM: Insufficient torque FE: Seat loose at customer site (S=8) FC: Torque gun out of calibration, missed tightening (O=4)
Action Direction
Prevention P: daily torque gun check, missed-tightening sensor Detection D: 100% torque + angle curve recording Re-rate S/O/D after optimization; confirm AP reduced
PFMEA Seven-Step Method — Practical Training

## Slide 10
04
Risk Analysis
AP Replaces "RPN-Only" Thinking

## Slide 11
S / O / D and AP (Illustration)
Dimension | What to Ask | Rating Points
S Severity | Impact on customer / next operation | Safety / regulatory / line stop → high S
O Occurrence | How likely the cause occurs | Historical data, maturity of preventive controls
D Detection | Difficulty of detecting failure before escape | Detection methods, auto line stop, etc.
AP | Action Priority H / M / L | High AP must have actions and appear on CP
PFMEA Seven-Step Method — Practical Training

## Slide 12
Prevention vs Detection
Prevention (P): mistake-proofing, parameter lock, SPC, calibration — preferred over detection
Detection (D): measurement inspection, 100% functional test, vision AI — tighten when needed
Myth: more detection is always better — costly, lagging, and does not remove root cause
Optimization actions must state: content, owner, target date, verification method
After actions, re-rate S/O/D to show AP has been reduced
PFMEA Seven-Step Method — Practical Training

## Slide 13
05
PFMEA → CP Linkage
Pairs with CP courseware in the library

## Slide 14
Field Mapping (PFMEA → Control Plan)
CP Column | From PFMEA
Process / Characteristic | Process step and functional requirements
Specification / Tolerance | Functional analysis output
Evaluation / Measurement | Detection controls
Sample / Frequency | Based on AP and capacity
Control Method | Prevention + Detection
Reaction Plan | Line stop / containment / notification per FE
PFMEA Seven-Step Method — Practical Training

## Slide 15
Linkage Rules
PFMEA update → CP review required (within 48h or per ECN process)
CP change → verify PFMEA still adequate
AP=H items: must appear on CP; frequency not weaker than PFMEA recommendation
Special characteristics: consistent symbols DFMEA → PFMEA → CP
Layered Audit: spot-check PFMEA actions on the shop floor
PFMEA Seven-Step Method — Practical Training

## Slide 16
06
Living PFMEA
Who Maintains in Production? When to Update?

## Slide 17
Trigger Events and PFMEA Actions
Trigger | Action
New process / new equipment | New or major PFMEA revision
4M change | Review and update (Man, Machine, Material, Method)
Major customer complaint / recall | Targeted re-analysis
Annual system review | Verify action effectiveness; close overdue items
Repeat defect | Trace root cause to FC; update prevention / detection
PFMEA Seven-Step Method — Practical Training

## Slide 18
Cross-Functional Team (Minimum)
Process / Manufacturing Engineering
Production / Team Leader
Equipment / ME
Quality / QE
Program / Customer Representative
PFMEA Seven-Step Method — Practical Training

## Slide 19
07
Common Pitfalls
Frequent Audit Nonconformities

## Slide 20
Pitfalls and Countermeasures
Pitfall | Countermeasure
Quality dept fills form alone | Cross-functional sign-off and shop-floor verification
RPN-only ranking | Use AP with FE red lines
PFMEA disconnected from CP | Mapping table + ECN linkage
Frozen when project ends | Assign process owner for maintenance
Actions without verification | Re-rate after optimization + data evidence
PFMEA Seven-Step Method — Practical Training

## Slide 21
Implementation Checklist
Complete seven-step outputs: boundary diagram, structure tree, failure chains, AP list
100% of AP=H items have actions, owner, date, verification record
CP and PFMEA versions cross-referenced consistently
4M change process includes PFMEA review gate
Pilot / production Layered Audit includes PFMEA action spot checks
PFMEA Seven-Step Method — Practical Training

## Slide 22
PFMEA Three Questions — Is the Loop Complete?
🔍
Identified?
📋
On the CP?
🔄
Updated for changes?
Summary
PFMEA seven-step method is structured thinking — from structure to function to failure to risk to optimization, then CP deployment: the process risk hub of the APQP package. Recommendation: pick one line operation; in 2 weeks complete a pilot "one PFMEA row → one CP row → shop-floor verification".
QTank · Companion CP courseware id=37

## Slide 23
Q & A
Related article: PFMEA Seven-Step Method and Control Plan Linkage · Knowledge Code 8.3.1

## Slide 24
Thank You
qtank.org
QTank
qtank.org