## Slide 1
PPAP Process Approval
Submission and Review — Practical Training
18 Elements · Submission Level · Linkage with PFMEA/CP Package
QTank
Knowledge Code 8.3.3 · PPAP and Process Approval Approach
qtank.org

## Slide 2
Training Objectives
After training, answer: Are all elements complete? Is data credible? Can production reproduce results?
Understand PPAP purpose in APQP and IATF 16949: prove process can consistently produce conforming parts
Master 18 submission elements and cross-references (DFMEA/PFMEA/CP/MSA/SPC)
Select correct submission level (1–5) and prepare PSW (Part Submission Warrant)
Recognize "complete files but unverified process" fake PPAP risk
Build awareness of re-submission and break-point management after 4M changes
PPAP Process Approval — Practical Training

## Slide 3
01
What Is PPAP?
Not finished when a folder is submitted

## Slide 4
Case: Customer Approved, Line Still Stopped
❌ Symptoms
• PPAP 18 elements "complete" and approved • First production week FTQ only 82% • Full dimension OK but process capability Ppk<1 • Cpk 1.67 cited without MSA
✅ Root Causes
• Initial study used trial-mold parts, not production rate • CP and shop-floor SOP version mismatch • PSW commitments disconnected from ongoing monitoring PPAP = process capability + document consistency evidence
PPAP Process Approval — Practical Training

## Slide 5
PPAP Purpose and Timing
Purpose: prove to customer that approved process consistently meets engineering specs
Typical timing: new product, new process, new site, major 4M change, restart after long shutdown
APQP phase gate: trial production (Phase 3) complete → PPAP submit → production approval
Core output: PSW + supporting package per level
IATF emphasis: CSR may tighten elements or sample size
PPAP Process Approval — Practical Training

## Slide 6
02
18 Submission Elements
AIAG PPAP Manual Core Checklist

## Slide 7
PPAP 18 Elements (1/2)
No. | Element | Key Points
1 | Design Records | Drawings/CAD including engineering changes
2 | Engineering Change Documents | Approved ECN
3 | Customer Engineering Approval | Customer sign-off / system status
4 | Design FMEA | DFMEA and special characteristics
5 | Process Flow Diagram | Consistent with PFMEA/CP operations
6 | Process FMEA | Living FMEA trial version
7 | Control Plan | Pre-production/production CP linked to PFMEA
8 | MSA Studies | Acceptable GR&R before citing measurement data
9 | Dimensional Results | Full dimension / functional dimension reports
PPAP Process Approval — Practical Training

## Slide 8
PPAP 18 Elements (2/2)
No. | Element | Key Points
10 | Material / Performance Tests | Consistent with DVP
11 | Initial Process Study | SPC/Cpk/Ppk; process in control
12 | Qualified Laboratory Documentation | ISO 17025 or customer accepted
13 | Appearance Approval | AAR (if applicable)
14 | Production Sample Parts | From production process / rate
15 | Master Sample | Customer-approved master
16 | Checking Aids | Fixture/tooling list and calibration
17 | CSR | Customer-Specific Requirements Compliance
18 | PSW | Part Submission Warrant signed
PPAP Process Approval — Practical Training

## Slide 9
03
Submission Level
How to Choose Level 1–5

## Slide 10
PPAP Submission Levels (Overview)
Level | PSW | Supporting Documents
1 | PSW only | No others (rarely used)
2 | PSW + samples | Limited data package
3 | PSW + samples | All 18 elements (most common)
4 | PSW + others | Per customer requirement
5 | PSW + samples | Full review at customer site
PPAP Process Approval — Practical Training

## Slide 11
PSW Completion Essentials
Statement: parts from production process meet all engineering specifications
Note: submission level, appearance items, chemical/material submission
Process name/number consistent with flow diagram and CP
If results do not meet spec: document deviation and customer approval on PSW
Sign-off level: usually customer engineering/quality approval before bulk supply
PPAP Process Approval — Practical Training

## Slide 12
04
Document Package Linkage
Pairs with PFMEA / CP courseware

## Slide 13
APQP Core Document Chain
DFMEA
PFMEA
Process Flow Diagram
CP
MSA
SPC
PPAP
PPAP Process Approval — Practical Training

## Slide 14
Audits often check "inconsistencies"
Check Point | Acceptance Criteria
Flow diagram vs PFMEA | Operation numbers match
PFMEA vs CP | AP=H has controls and reaction plan
CP vs SOP | Version and frequency consistent
MSA vs dimensional/SPC | Gauge GR&R acceptable
Samples vs reports | Same lot / same process
PPAP Process Approval — Practical Training

## Slide 15
05
Initial Process Study
Element 11 most prone to "looks fake"

## Slide 16
Cpk/Ppk and PPAP
Submission Requirements
Process in control (stable control chart) Subgroups represent production rate Typically Cpk/Ppk ≥ 1.67 (per CSR) Strong conclusions only after MSA pass
Production Risk
25 trial-mold subgroups ≠ production variation Long-term Ppk below PPAP commitment → customer tightens sorting / stops supply Must establish ongoing SPC monitoring
PPAP Process Approval — Practical Training

## Slide 17
06
4M Changes and Re-submission
Approval is not "permanent exemption"

## Slide 18
Changes Trigger PPAP Actions
Change | Typical Requirement
New supplier / new material | Re-PPAP or per CSR
Major equipment / tooling change | At least partial element update
Process parameter / location change | Re-evaluate PFMEA/CP/SPC
Design change | DFMEA→PFMEA→CP cascade
Restart after long shutdown | Customer may require re-submission
PPAP Process Approval — Practical Training

## Slide 19
Run@Rate / Trial Production Verification
Trial production parts must come from **approved process** (not hand-built samples or R&D machines)
Run@Rate: continuous production at production rate; verify capacity and quality stability
Sample retention: lot ID, traceable to process parameter records
Link to break-point changeover (8.4.2): old stock disposition, new revision effective date
Pass internal PPAP checklist before customer submission
PPAP Process Approval — Practical Training

## Slide 20
07
Common Pitfalls
Fake Completeness vs True Approval

## Slide 21
Pitfalls and Countermeasures
Pitfall | Countermeasure
Folder completeness is enough | Reproduce on shop floor per CP + data verification
Copy old product PPAP | Rebuild PFMEA/CP/SPC for new process
Skip MSA | GR&R first, then report Cpk
PSW disconnected from CSR | Check CSR matrix item by item
No updates after approval | 4M changes trigger review
PPAP Process Approval — Practical Training

## Slide 22
PPAP Self-Check List (Excerpt)
18 elements complete per level; version cross-references consistent
PFMEA/CP/SOP three-way check done; special characteristics transferred correctly
Acceptable MSA reports cover PPAP gauges
Initial process study: subgroup rules, control chart, capability indices explained
Sample lot traceable to full dimension/test reports
PSW matches actual submission; customer sign-off path clear
PPAP Process Approval — Practical Training

## Slide 23
PPAP Three Questions — Does Approval Hold Up?
📁
All elements complete?
📊
Is data credible?
🏭
Can production reproduce results?
Summary
PPAP is APQP's "process approval gate" — linking PFMEA, CP, MSA, SPC into a customer-auditable evidence chain. Recommendation: use this courseware + PFMEA/CP companions for an internal mock audit before customer submission.
QTank · tank folder includes PPAP Excel template pack

## Slide 24
Q & A
Companion: PFMEA (id=38) · CP (id=37) · Knowledge Code 8.3.3

## Slide 25
Thank You
qtank.org
QTank
qtank.org