## Slide 1
Lean Production Practical Training Workbook
Core tools: 5S/TPM/VSM/SMED/kanban with 10+ case studies — for production managers and lean champions
QTank
Knowledge Code 7.1.1 · VSM Value Stream Mapping
qtank.org

## Slide 2
bdjson not found
Table of contents
CATALOGUE
01
Lean Manufacturing Overview
02
Explanation of core lean tools
03
Value Stream Mapping (VSM) Application
04
continuous improvement approach
05
Lean production implementation strategy
06
Enterprise practical case analysis

## Slide 3
01
Lean Manufacturing Overview

## Slide 4
Definition and core concepts
The core goal of lean production is to identify and eliminate seven types of waste (overproduction, waiting, transportation, overprocessing, inventory, movement, defects) in the production process to achieve optimal allocation of resources.
Eliminate waste
Through the PDCA (plan-do-check-act) cycle and Kaizen (improvement) culture, we continuously optimize processes and improve efficiency and quality.
Continuous Improvement
Emphasize the participation and empowerment of front-line employees, and stimulate the team's enthusiasm for proactive improvement through standardized operations and problem-solving training.
Respect employees
Establish a continuous flow production system, reduce inventory through the pull mechanism, and achieve on-demand production.
flow and pull
All activities are centered around creating value for customers, avoiding non-value-added activities and ensuring that resource investment is directly related to customer needs.
customer value orientation

## Slide 5
1937
1973
digital transformation
The COVID-19 pandemic has accelerated the application of lean tools in the cloud and digital twins.
2001
2020
Lean Six Sigma
Motorola combines Lean and Six Sigma to form an improvement methodology.
oil crisis
The global energy crisis has highlighted the efficiency of Toyota's production method and attracted industry attention.
Toyota was founded
Toyota Motor Industry Co., Ltd. was established, laying the foundation for lean production organization.
Toyota Origins
milestone
The birth of JIT
1953
1990
2010
Industry 4.0 Convergence
Lean production and intelligent manufacturing technology have begun to develop in depth.
Lean naming
"The Machine That Changed the World" first proposed the term 'lean production'.
Kanban system
Ohno Taiichi implemented pull-type production kanban for the first time in Toyota workshops.
TPS formation
Global promotion
History and development

## Slide 6
The importance of lean production
cost reduction
By reducing waste and improving efficiency, raw materials, inventory and labor costs can be significantly reduced, and companies can save an average of 15%-30% in operating expenses.
01
Quality improvement
Standardized operations and defect prevention mechanisms (such as error-proofing design) can reduce product defect rates by more than 50%.
02
Shortened lead times
Flow optimization can shorten the production cycle by 30%-70% and quickly respond to changes in market demand.
03
Increased employee engagement
The problem visualization and improvement proposal system enhances employees' sense of belonging and reduces turnover rates.
04
Strengthening competitive advantage
Flexible production capabilities help companies adapt to the trend of small batch customization and seize market opportunities.
05
Risk management and control
Expose process bottlenecks through value stream mapping (VSM) to avoid supply chain disruption or overcapacity risks in advance.
06

## Slide 7
02
Explanation of core lean tools

## Slide 8
01
02
04
03
05
06
Sort (Seiri)
Set in Order (Seiton)
Shine (Seiso)
Identify problems and improvement opportunities in current 5S management through on-site observation.
Visual inspection
Problem rectification
Standard cure
Sustain (Shitsuke)
Safety
Standardize (Seiketsu)
Diagnosis of current situation
Develop clear 5S implementation goals and acceptance criteria based on diagnostic results.
goal setting
Prepare a detailed 5S promotion plan, including division of responsibilities, time nodes and resource requirements.
Plan making
Divide the site into several 5S management responsibility areas according to functions or scope of responsibilities.
Regional division
Separate and handle all items on site between essential items and non-essential items.
Item classification
Implement standardized placement management of tools, materials and other items through identification and positioning.
Fixed-Location Management
Implementation steps
Effect verification
5S Shopfloor Management

## Slide 9
Autonomous maintenance
Operators participate in the daily maintenance of equipment, such as cleaning, lubrication, and inspection, to enhance their understanding of the equipment and reduce sudden failures.
Planned maintenance
Develop a preventive maintenance plan to regularly inspect and maintain equipment to extend equipment life and reduce downtime and repair costs.
quality maintenance
Reduce quality fluctuations in the production process through equipment maintenance, ensure product consistency, and reduce the rate of defective products.
early management
Consider maintenance needs during the introduction stage of new equipment, optimize the design, and reduce the difficulty and cost of subsequent maintenance.
Education and training
Conduct TPM concept and skills training for employees to enhance the maintenance awareness and capabilities of all employees and form a culture of continuous improvement.
safe environment
Eliminate safety hazards, improve the working environment, and ensure employee health and production safety through TPM management.
TPM — Total Productive Maintenance
01
02
03
04
05
06

## Slide 10
Quick Changeover (SMED)
Divide mold changing operations into internal operations that must be performed during shutdown and external operations that can be completed while the equipment is running to reduce downtime.
01
By optimizing processes and tools, some internal tasks, such as mold preheating, tool preparation, etc., can be completed earlier or later.
02
Parallel jobs
Arrange multiple people to perform the mold change operation at the same time to shorten the overall time, but ensure the safety and coordination of the operation.
03
Develop detailed mold change operation standards to reduce adjustment and trial and error time, and improve mold change efficiency and consistency.
04
Use hydraulic, pneumatic and other quick clamping tools to reduce the time required for traditional bolt fixing.
05
Convert internal jobs to external jobs
Use quick clamping device
Standardized Work
Differentiate between internal and external work

## Slide 11
Kanban signals trigger the production of upstream processes to avoid overproduction and reduce inventory waste.
Pull Production
Control the quantity of work-in-progress during the production process through kanban quantity to avoid overproduction and waste of resources.
Limit the quantity of work in progress
Kanban cards or electronic kanban visually display production progress, inventory levels and problem points to facilitate quick decision-making.
Visual Management
01
03
02
Kanban Management System
The Kanban system can quickly expose production anomalies, such as delays or quality issues, prompting the team to resolve them promptly.
Exception response mechanism
Extend the Kanban system to suppliers to achieve synchronized production and accurate material distribution in the supply chain.
Supply chain collaboration
By analyzing Kanban data, process bottlenecks and improvement opportunities are discovered to promote production efficiency and quality improvements.
Continuous Improvement
04
06
05

## Slide 12
03
Value Stream Mapping (VSM) Application

## Slide 13
value stream definition
Separation analysis of material flow and information flow
Type breakdown
future state diagram
Current state diagram
Basic concepts and types of VSM
Value flow refers to the sum of all value-added and non-value-added activities in the entire process from raw materials to finished products delivered to customers, covering the dynamic interaction of information flow and material flow.
By visualizing each link in the existing production process, waste (such as waiting, handling, inventory, etc.) is identified, providing a baseline for subsequent optimization.
The ideal process designed based on lean principles clearly defines the target path to eliminate waste, including core improvement directions such as cycle time matching and continuous flow establishment.
Distinguish between material flow (such as processing, transportation) and information transmission (such as orders, plans), and reveal the efficiency bottleneck caused by the disconnect between the two.
It includes macro VSM (cross-departmental level) and micro VSM (process level). The former focuses on overall collaboration, while the latter focuses on local detail optimization.

## Slide 14
Determine product family
Timeline calculation
root cause analysis
symbol standardization
On-site data collection
VSM drawing and analysis steps
Select representative products or service families to ensure focused analysis and avoid resource dispersion. The PQPR analysis method (product-quantity-process route) is usually used to screen key objects.
Record cycle time, changeover time, work-in-progress inventory and other data through on-site observation to ensure that the information truly reflects the actual operating status.
Use unified icons (such as inventory triangles, push arrows, kanban symbols) to draw processes, and follow internationally accepted VSM graphic specifications to enhance readability.
Mark value-added time and non-value-added time at the bottom of the chart, calculate process efficiency (proportion of value-added time), and quantify room for improvement.
Combined with the fishbone diagram or the 5Why method, discover the underlying reasons behind waste (such as unreasonable equipment layout, plan fluctuations, etc.).

## Slide 15
process analysis
Identify key process nodes in the value stream, analyze value-added and non-value-added activities in each link, clarify optimization priorities, eliminate waste, and improve overall process efficiency.
01
standardization
Establish standardized operating procedures, unify operating specifications, reduce variation and waste, and ensure process stability and repeatability.
03
Beat optimization
By adjusting the production cycle time, the production capacity of each process is balanced, bottlenecks are eliminated, and the continuous flow and efficiency of the production line are maximized.
02
pull system
Implement pull production control to trigger upstream production based on downstream demand, reduce work-in-process inventory, and improve response speed.
04
Continuous Improvement
Establish a continuous improvement mechanism, regularly evaluate optimization effects, implement PDCA cyclically, and promote continuous optimization of value streams.
06
Visual management
Use visualization tools such as Kanban boards to monitor process status in real time, quickly identify anomalies and take corrective measures.
05
Achieve efficient flow of value streams, eliminate waste, and improve overall operational efficiency
VSM optimization practical skills

## Slide 16
04
continuous improvement approach

## Slide 17
Full Employee Participation
Kaizen emphasizes comprehensive participation from top managers to front-line employees, and achieves continuous improvement through small steps to ensure that every link can be optimized.
Focus on small improvements
Unlike large-scale changes, Kaizen focuses on accumulating significant efficiency improvements through countless small improvements, such as adjusting workstation layout to reduce wasted movement.
Standardized process
After each improvement, the standardized work instructions must be updated in a timely manner to ensure that the improvement results are solidified and promoted to other similar links.
Continuous training
Regularly organize employees to participate in training on Kaizen tools and methods, such as 5S management, value stream map analysis, etc., to improve the team's problem discovery and solution capabilities.
Visual Kanban
Display improvement progress and results in real time through Kanban management, create a cultural atmosphere of continuous improvement, and encourage employees to proactively propose improvement suggestions.
Kaizen continuous improvement
01
02
03
04
05

## Slide 18
  Quality cost visualization: The waste of defective repairs directly erodes profit margins, and quality cost accounting needs to be used to promote the quality awareness of all employees.
  Dialectics of Process Accuracy: Over-processing reflects excess technology, and a customer demand-oriented process standard system should be established.
  micro-movement economics: The cumulative effect of 12 types of action waste is significant, and the optimization of IE techniques can increase human efficiency by more than 15%.
  Logistics value reconstruction: Handling waste exposes factory layout defects, and value stream map analysis is a key tool for improvement.
  Inventory paradox cracked: Inventory buffering masks problems, and the vicious cycle needs to be broken through balanced production.
waste type | Specific performance | Improvement measures
Waste of bad repairs | Disposal of defective products results in loss of materials/man-hours and loss of credibility | Strengthen process quality control and establish error prevention mechanisms
Over processing and waste | Unnecessary high-precision processing and redundant energy consumption | Standardized process parameters to match actual customer needs
Wasted action | 12 types of invalid actions (such as one hand idle/turning too large) | Implement the principle of action economy and optimize the layout of workstations
Moving waste | Invalid movement of materials leads to waste of space/time/manpower | Adopt U-shaped production line and implement single-piece flow
Inventory waste | Occupy funds, increase warehousing costs, risk of material depreciation | Implement JIT production and shorten changeover time
Waste identification and elimination

## Slide 19
05
Lean production implementation strategy

## Slide 20
beat control
Parameter settings
Tool selection
Scheme design
Implementation by all staff
Standard setting
priority
Customer needs
Requirements confirmation
process chain
Waste point
value stream
Current situation analysis
The key is to do it
Focus on execution
Continuous improvement
Project start
Standard implementation
Effect verification
Experience solidified
Comprehensive promotion
Full Employee Participation
Problem improvement
Continuous optimization
simulated production
Selected items
Pilot operation
Implementation steps and processes

## Slide 21
Skill improvement
Capability building
Carry out cross-functional job rotations to cultivate multi-skilled workers and a sense of collaboration.
Systematically study lean tools and methods and master standardized work skills.
Pre-job training ensures employees understand lean concepts and basic norms.
01
Strengthen on-site improvement capabilities through special training such as 5S and TPM.
02
Develop value stream analysis capabilities and establish a continuous improvement mindset.
03
Executives need to be proficient in lean strategic planning and change management methods.
04
Organize Lean Salons to share best practices and innovative cases.
01
Reserve a team of lean internal trainers and inherit the core methodology.
02
Train the team to use A3 reports to solve practical problems.
03
Leaders need to master lean culture shaping and organizational empowerment skills.
04
decision-making level
backbone layer
growth period
Execution layer
Personnel training and development

## Slide 22
high-level commitment
cultural change
Link lean improvement results with employee performance, design material and non-material reward programs, and maintain team participation enthusiasm.
Incentive mechanism
Always take customer needs as the starting point, regularly collect customer feedback and convert it into internal improvement projects to ensure that lean improvements create actual value.
customer oriented
Establish an indicator monitoring system covering quality, efficiency, cost and other dimensions, use data to quantify improvement effects, and avoid subjective decision-making.
data driven
The top management of the company must personally participate in lean promotion, provide resource support and regularly review progress to ensure consistency between strategy and execution.
Promote a shift from a "blame culture" to a "problem-solving culture", encourage exposing problems rather than covering them up, and build psychological safety.
Key factors for success

## Slide 23
06
Enterprise practical case analysis

## Slide 24
Improve activity workshop efficiency by 30% through 5S
Problem 1: Unclear identification
Difficulty positioning the area identification blur tool
Implement a color signage management system
1
Establish an item positioning billboard system
2
Problem 3: Missing cleaning
Equipment oil and dust accumulation affect accuracy
Develop equipment cleaning standards
1
Establish inspection and maintenance process
2
Problem 2: Insufficient organization
There is a serious accumulation of idle items on site
Carry out essential goods identification activities
1
Implement regular cleaning cycles
2
Problem 4: Lack of literacy
Employees habitually violate regulations
Prepare visual operation manual
1
Carry out OPL single-point education
2
Case 1: 5S implementation optimization
Improvement: red card combat
Improvement: Standardization
Improvement: visual management
Improvement: Responsibility partitioning

## Slide 25
Case 2: VSM process improvement
Current value stream mapping
future state design
Implementation plan development
Pilot and promotion
employee participation mechanism
Collaborate across departments to collect data, identify waste points in the entire process from raw materials to finished products, such as inventory backlogs, waiting times, etc., and mark timelines and resource consumption.
Replan the process based on lean principles, merge redundant links, introduce unitized production layout, shorten the delivery cycle, and aim to reduce the proportion of non-value-added activities by more than 40%.
Prioritize bottleneck processes, such as reducing changeover time through rapid mold change (SMED) technology, while establishing a buffer inventory strategy to balance production fluctuations.
Select typical production lines for pilot improvements. After verifying the results, gradually expand to the entire factory, and establish a KPI monitoring system to ensure that the improvement results are sustainable.
Organize VSM workshops to train front-line employees to use improvement tools, encourage them to make optimization suggestions, and create a bottom-up improvement atmosphere.

## Slide 26
Case 3: Kanban system application
Kanban type selection
Choose dual-card kanban (production-handling) or electronic kanban according to material characteristics, and clarify signal triggering rules, such as minimum inventory and replenishment cycle, to achieve pull-type production.
Visual design
Use color to distinguish priorities (red/yellow/green), combined with digital display of real-time inventory status, to ensure intuitive information transmission and reduce communication errors.
Exception response process
Set up an abnormal kanban alarm mechanism to automatically notify the responsible person when there is a shortage of materials, and set a response time limit of 30 minutes to avoid production interruptions.
Multi-level Kanban collaboration
Integrate supplier dashboards and internal production dashboards to synchronize the supply chain and shorten the raw material procurement cycle to within 48 hours.
Continuous optimization and iteration
Analyze kanban data (such as turnover rate, dead time) every month, adjust parameters or rules, and gradually reduce the number of kanbans by 20% to reduce system complexity.

## Slide 27
Thank You
qtank.org
QTank
qtank.org