## Slide 1
Process Performance
& Process Audit Practical Training
From lagging KPIs to real process approach · IATF / VDA 6.3 mindset
QTank
Knowledge Code 2.2.2 · Process Performance & Process Audit
qtank.org

## Slide 2
Training Objectives
After training you should answer: is the process stable? is the design sound?
Separate result KPIs from process KPIs; build predictable process capability
Design value stream performance boards with action thresholds (yellow/red)
Master six-step process audit and differences vs LPA and product audit
Build process register linking performance exceptions to tightened audits
Run a simplified process audit and output improvement items
Process Performance & Process Audit Training

## Slide 3
01
Process Performance
Don't wait for complaints to read the numbers

## Slide 4
Lagging vs leading indicators
❌ Results only
• Complaints, PPM, warranty cost — react only after failure • Monthly reports; front line disconnected • Departments optimize locally; value stream breaks
✅ Process performance
• FPY, Cpk, deviation close cycle, first piece after changeover • Shift/daily/weekly updates driving fast response • Process owner = value stream lead
Process Performance & Process Audit Training

## Slide 5
Three-tier metric structure
Tier | Example | Purpose
Results tier | Complaints, PPM, OTD | Management & customer dialogue
Process tier | FPY, SPC out-of-control count, LPA compliance rate | Daily management & prediction
Driver tier | Training completion rate, on-time calibration rate | Capability building
Process Performance & Process Audit Training

## Slide 6
Process KPI reference library (excerpt)
Production: FPY/RTY, OEE breakdown, first-piece defect rate after changeover
Quality: NCR close cycle, repeat NCR, deviation trend by risk tier
Supply chain: incoming PPM, SCAR response cycle
5–7 core KPIs per value stream; each must have an owner
Define yellow/red thresholds and DRI per KPI — not report-only
Process Performance & Process Audit Training

## Slide 7
Three-tier boards & management cadence
Team board (per shift)
Value stream daily (15 min)
Plant / function weekly
Process Performance & Process Audit Training

## Slide 8
02
Process audit
Verify process can consistently produce conforming output

## Slide 9
Three audit types — roles
Type | Question asked | Method
System audit | Does it meet standard requirements? | Sample procedures & documents
Product audit | Does product meet specification? | Measure per specification
Process audit | Is process stable? Is design sound? | Walk-through + performance + on-site
Process Performance & Process Audit Training

## Slide 10
Six-step process audit
1. Select process (risk-based)
2. Review planning (CP/FMEA)
3. Review performance (SPC/FPY)
4. On-site verification
5. Score & classify
6. Improve & re-audit
Process Performance & Process Audit Training

## Slide 11
On-site verification essentials
Walk-through: trace 1–2 samples input to output
Triangle check: listen (interview) → see (floor) → check (records)
KCP check: criteria clear? escalation path? error-proofing effective?
Interface audit: upstream/downstream I/O, SLA, escalation
Data-driven focus: review 6–12 month SPC/FPY trends first
Process Performance & Process Audit Training

## Slide 12
03
Linked closed loop
Performance red → tighten audit → improve → recover

## Slide 13
Process Register
Fields: process name, owner, process KPI, last audit, next planned, risk level
Performance red → trigger tightened process audit or focused diagnostic
Audit finding → CAPA/improvement project → update FMEA/CP
KPI recovered → audit frequency may relax (risk-based)
LPA checks daily execution; process audit checks CP adequacy — complementary
Process Performance & Process Audit Training

## Slide 14
Common pitfalls
❌ Avoid
• Process KPIs visible only to quality • Skip audit when Cpk looks good • Audit scoring with no improvement • Performance and audit in separate meetings
✅ Recommended
• Value stream owner owns process KPIs • Documents and shop floor may diverge • Improvement projects + data verification • Integrate into value stream daily meeting
Process Performance & Process Audit Training

## Slide 15
90-day launch path
Weeks 1–3: pick one value stream; define 5 process KPIs + daily board
Weeks 4–6: build process register; first simplified audit on worst process
Weeks 7–12: close 2 improvement projects and verify KPIs; train 2 internal auditors
Related article: Process Performance & Process Audit (Knowledge Code 2.2.2)
Process Performance & Process Audit Training

## Slide 16
Q & A
Related article: Process Performance & Process Audit — from lagging KPIs to real process approach qtank.org/article?id=143

## Slide 17
Thank You
qtank.org
QTank
qtank.org