## Slide 1
Recall & Crisis Communication
Practical Training
72-hour golden rhythm · traceability · compliance · unified messaging
QTank
Knowledge Code 10.2.3 · Recall & Crisis Communication Essentials
qtank.org

## Slide 2
Training Objectives
After training you should answer: who to trace? what to say? who speaks?
Understand harm assessment for recall triggers and Go/No-Go decision process
Master traceability, affected scope calculation, and crisis RACI
Know 72-hour crisis communication rhythm and spokesperson protocol
Use templates for customer notice, FAQ, internal hold order, etc.
Link to 8D and complaint systems; maintain annual drill discipline
Recall & Crisis Communication Training

## Slide 3
01
When to recall
Based on harm, not "how loud the noise is"

## Slide 4
Harm classification & response direction
Level | Typical situation | Action
Safety / regulatory | Personal injury, mandatory standard violation | Immediate recall + regulatory report
Function / performance | Cannot perform stated function; customer line stoppage | Negotiate replacement / conditional recall
Compliance / labeling | Label error, traceability gap | Limited recall or correction notice
Minor | Appearance/packaging; no safety impact | Usually service remedy, not recall
Recall & Crisis Communication Training

## Slide 5
Three decision principles
Conservative: when evidence is incomplete, expand containment first, then narrow scope
Single entry: cross-functional crisis team written Go/No-Go; no sales-side private settlements
Timestamp: regulatory response clock starts at first knowledge of potential harm
Maintain regulatory matrix: FDA, EU GPSR, SAMR, etc.
Complaint system "safety flag" auto-escalates to quality director
Recall & Crisis Communication Training

## Slide 6
02
Five nets in peacetime
Don't start from zero when crisis hits

## Slide 7
Five recall readiness nets
① Traceability net: forward/reverse; quarterly SN look-back drill within 4 hours
② Affected scope: cutover, BOM explosion, five-way tally (stock/in transit/at customer/etc.)
③ Crisis RACI: single spokesperson; technical experts don't give separate interviews
④ Communication template library: customer letter, dealer guide, regulatory report, FAQ
⑤ Reverse logistics: return inspection, scrap/rework, environmental compliance
Recall & Crisis Communication Training

## Slide 8
03
72-hour rhythm
Fast, accurate, steady

## Slide 9
Hours 0–24: control & alignment
Activate crisis team + hourly briefing
Internal hold order: stop shipment; assess line stoppage
Initial affected scope v0.1
External: acknowledged / investigating / will update / single contact
Recall & Crisis Communication Training

## Slide 10
Hours 24–72: notification & execution
Regulatory reporting (if applicable)
Formal customer/dealer notice + lot list
War room hotline on duty
Track completion rate; proactively issue second notice if scope expands
Recall & Crisis Communication Training

## Slide 11
04
Communication principles
What to say, how to say it, who speaks

## Slide 12
Messaging DO / DON'T
Do | Don't
Facts + actions already taken | Speculate on root cause; blame customer/supplier
State next steps and timeline | Prolonged silence with no updates
Distinguish known / unknown / under investigation | State uncertainty as certainty
Single spokesperson + FAQ | Multiple voices saying different things
Recall & Crisis Communication Training

## Slide 13
Channels & public sentiment
B2B
• Account manager 1-on-1 + formal letter • Priority phone calls for key accounts • Portal announcement as backup
B2C / internal
• Website, SMS, dealer posters • Employees hear from supervisors first • Monitor social media; respond within 24h
Recall & Crisis Communication Training

## Slide 14
8D linkage & closure metrics
Recall closure requires: 8D/LL, verified root-cause actions, archived communications
Metrics: notice delivery rate, recall completion rate, cycle time, scope expansion count
Closure: hazard eliminated + completion rate met + regulatory case closed (if applicable)
Drills: desktop annually; full-scale every 2 years
Related article: Recall & Crisis Communication (Knowledge Code 10.2.3)
Recall & Crisis Communication Training

## Slide 15
Q & A
Related article: Recall & Crisis Communication — 72-hour golden rhythm & external messaging control qtank.org/article?id=141

## Slide 16
Thank You
qtank.org
QTank
qtank.org