## Slide 1
QE empowerment training
Panoramic actual combat of QC to QE · Overview of role transformation and tools and methods
From "gatekeeping inspection" to "process design and system improvement" · Theory + Practical Operation · Job Competency Model
QTank
Knowledge No. 13.2.1 · Job Competency Model
qtank.org

## Slide 2
training objectives
Applicable objects: Excellent QC promoted to QE, new QE, internal training for quality supervisors
Establish QE (quality engineer) role awareness: boundaries and collaboration with QC, SQE, and PQE
Understanding QC→QE Turnaround: Thinking Mode, Time Allocation, and Capability Jump Path
Master the core areas of QE responsibility: Advanced Quality, Process Control, Problem Solving, Supplier and Customer Quality
Systematic review of essential QE theories: Deming/Juran/Crosby, PDCA, ISO 9001 seven principles
Proficient in selecting methods and tools: 8D/A3, Seven Tools, FMEA/CP/SPC/MSA/PPAP, DOE Getting Started
Complete the 90-Day Turnaround Action Plan and Self-Assessment Checklist
QE empowerment training · QC→QE panoramic practice

## Slide 3
Course map (recommended 2 to 3 days of intensive training + 90 days of on-the-job coaching)
module | theme | Duration reference
01～03 | Role transformation and competence | 0.5 days
04～05 | Quality theory and system | 0.5 days
06～09 | Advanced Quality and Core Tools | 1 day
10～14 | Problem Solving and Statistical Methods | 0.5 days
15～18 | supply chain, customers, change | 0.5 days
19～22 | Digital, Soft Skills, 90 Day Plan | 0.5 days
QE empowerment training · QC→QE panoramic practice

## Slide 4
01
opening case
The three months when QC rose to QE were "acclimated"

## Slide 5
Case: The inspection team leader of a Tier 2 machining factory was promoted to QE
❌ turn around dilemma
• Still monitor the inspection station every day, and drag 8D to the customer’s reminder • I couldn’t get a word in during the PFMEA meeting and just said “can’t detect it.” • Repeated problems with incoming materials from suppliers will only tighten IQC • Process parameter changes were not notified, and the CP version was lagging behind • Supervisor’s comment: “Still QC thinking, lacking engineering perspective”
✅ Turn around and break through
• Time allocation: Inspection 20% → Process Planning 40% • Leading the PFMEA→CP alignment pilot of a production line • Use 5Why+Fishbone to close 1 repeat customer complaint • Establish supplier PPAP issue list, SQE joint audit • Be independently responsible for the APQP quality nodes of new projects after 3 months
QE empowerment training · QC→QE panoramic practice

## Slide 6
Case Enlightenment: QE is not “Advanced QC”
QC Core: Determination of qualification, implementation of inspection standards, recording and isolation
QE Core: Define how to control, design control plans, promote root cause elimination and system prevention
Common reasons for failure in turnaround: unclear responsibilities, lack of tool and method training, no mentor, and still being kidnapped by test KPIs
Keys to successful turnaround: clear 90-day goals, project-based experience, cross-functional visibility (process/production/procurement)
The goal of this courseware: to give you a panoramic map of QE to avoid "getting promoted and still working in the same position"
QE empowerment training · QC→QE panoramic practice

## Slide 7
QC / QE / SQE / PQE Role Comparison (Getting Started)
Role | focus | Typical output
QC | Inspection execution and judgment | Inspection records and isolation of defective products
QE | Process planning and improvement | FMEA/CP/SPC, 8D, process capabilities
SQE | Supply chain quality | Supplier audit, PPAP, SCAR
PQE | Project advance quality | APQP deliverables, stage gate reviews
QE empowerment training · QC→QE panoramic practice

## Slide 8
02
QC→QE turn around
Three switches of thinking, time and ability

## Slide 9
Thinking model comparison
Dimensions | QC thinking | QE thinking
problem perspective | Found bad | Prevent adverse events
Data usage | Judge pass/fail | Find sources of variation and computing power
Standard source | Acceptance has been given to the standard | Participate in formulating/verifying the rationality of standards
Improve depth | Pick/Return | Root cause + systematic correction and prevention
Scope of collaboration | Inside the inspection station | Across processes, production, purchasing, and customers
Success Metrics | Missing detection rate and efficiency | PPM, Cpk, duplicate issue closure rate
QE empowerment training · QC→QE panoramic practice

## Slide 10
Time allocation turnaround (example)
Promoted to QC monitor (week)
• 60% refund on on-site inspection and judgment • Records and Reports 25% • Training new employees 10% • Others 5%
QE after turning around (target)
• Process Planning/Documentation 35% (FMEA/CP/SPC) • Problem Solved 25% (8D/CAPA) • Review with Gemba 20% • Project/Supplier/Customer 15% • Inspection support 5% (exceptional not routine)
QE empowerment training · QC→QE panoramic practice

## Slide 11
QC→QE turnaround path (recommended 90 days)
role clarification
Tools to make up lessons
Follow the project
independent and responsible
Review certification
QE empowerment training · QC→QE panoramic practice

## Slide 12
Turn around support: What to do on the organizational side
Release of JD and RACI: What is no longer routinely checked by QE
Designated mentor (senior QE/quality manager) 1on1 once a week
First project: small scope, quantifiable (such as a line CP alignment or an 8D)
Adjust KPI: From "inspection workload" to "process indicator + project closure"
Training records are included in **13.2.2 Training system and effect evaluation**
QE empowerment training · QC→QE panoramic practice

## Slide 13
Turn around and evaluate yourself: Am I still a QC?
self-evaluation items | Still QC mode | Already in QE mode
Customer complaint is coming | Check first | First containment + root cause + horizontal expansion
Bad incoming materials | Full inspection | Supplier evaluation + specification change + PPAP
Meeting | With inspection data | With process capability + improvement plan
document | Read only SOP | Maintain FMEA/CP version
QE empowerment training · QC→QE panoramic practice

## Slide 14
03
QE role awareness
Position in the value chain

## Slide 15
QE definition (used in this courseware)
Quality Engineer (QE): Use engineering methods and quality tools to keep products/processes under control and continuously improved during design, manufacturing and delivery.
Keywords: engineering, prevention, data-driven, cross-functional, documented evidence
It is not equal to: a quality clerk who only writes reports; nor is it equal to a "firefighter" who takes the blame for production.
IATF/auto chain: QE often serves as a PQE node or is deeply involved in APQP
Medical/Electronics: QE focuses on verification, traceability, change and CAPA regulatory compliance
QE empowerment training · QC→QE panoramic practice

## Slide 16
QE’s six major areas of responsibility
Responsibility area | Main content | Typical deliverables
Advance planning | VOC, special characteristics, DFMEA/PFMEA | APQP node file
process control | CP, SPC, MSA, response plan | Controlled process, capability reporting
Inspection planning | IQC/IPQC/FQC scheme | Sampling plan, inspection tool list
problem solving | 8D、5Why、A3、CAPA | Root cause evidence, recurrence prevention
supply chain | Second-party audit, SCAR, PPAP | Supplier performance, approval status
customer interface | Audit response, PPAP, changes | Submit package, issue closure evidence
QE empowerment training · QC→QE panoramic practice

## Slide 17
QE's position in the quality value chain
upstream (input)
• Customer CSR/Drawings/Regulations • VOCs and special characteristics • Design output, DFMEA • Supplier incoming materials and PPAP
Downstream (output)
• Controlled process and CP execution • Traceable batch/SN records • Capability index and audit evidence • Post-launch failure feedback closed loop
QE empowerment training · QC→QE panoramic practice

## Slide 18
Stakeholder map
Production/manufacturing: SOPs, response plans, line shutdown rights and upgrade paths must be aligned in advance
Process/R&D: Co-Owner of PFMEA, Special Features, Change ECN
Purchasing/SQE: Incoming material specifications, supplier approval, SCAR and IQC standards consistent
Laboratory: MSA, gauge calibration, OOS/OOT disposal
Client/Auditor: PPAP, 8D, process capabilities, document version consistency
QE’s “soft power” comes from professionalism and evidence, not just rank
QE empowerment training · QC→QE panoramic practice

## Slide 19
QE collaborates with relevant positions RACI (Simplified)
Activity | QE | QC | Craftsmanship | Production
Write PFMEA | R | C | R | C
Writing a CP | R | C | C | I
Daily inspection | C | R | I | I
8D Dominance | R | C | C | C
SPC runaway reaction | A | C | C | R
QE empowerment training · QC→QE panoramic practice

## Slide 20
04
QE competency model
Knowledge · Skills · Behavior · Experience

## Slide 21
QE capability four quadrants
Quadrant | content | Assessment method
Knowledge | Standards, regulations, statistical basis | Written test/certification
Skill | FMEA, 8D, SPC, audit | Practical exercises + projects
Behavior | Communication, promotion, systematic thinking | 360°/instructor observation
experience | Industry products and process types | Project resume
QE empowerment training · QC→QE panoramic practice

## Slide 22
Hard skills list (L1→L3)
Skill | L1 Getting Started | L2 independent | L3 Expert
PFMEA/CP | Can fill in forms | Leading process | Review others, methodology
SPC/MSA | Can read pictures | Map construction and difference | Measurement uncertainty
8D/A3 | participate | dominant close | Teach others, systematize
Sampling inspection | Lookup table execution | planning plan | risk modeling
APQP/PPAP | Known node | Submit document package | customer negotiation
QE empowerment training · QC→QE panoramic practice

## Slide 23
Soft skills checklist
Skill | QE scenario | training method
structured expression | 8D reporting, review response | Pyramid Principle Exercise
Cross-departmental promotion | CP landing and line suspension decisions | RACI project
coaching questions | 5Why guides production | role play
Priority management | Multiple customer complaints concurrently | Eisenhower matrix
Customer thinking | PPAP controversy | Case study
QE empowerment training · QC→QE panoramic practice

## Slide 24
Training Effect Level 4 (Kirkpatrick)
L1 response: Do students find it useful? (After-class questionnaire)
L2 learning: Can you get it right in taking the FMEA/SPC exam? (Closed book + computer)
L3 Behavior: Will you submit CP/8D independently within 90 days? (Supervisor observation)
L4 Results: Did PPM, duplicate issues decrease? (Business Metrics)
QC→QE training cannot stop at L1 - it must be bound to L3 project acceptance
QE empowerment training · QC→QE panoramic practice

## Slide 25
Competency Assessment: Practical Exercise Design
Walkthrough 1 (Day1 Afternoon)
Given customer complaint description → completed within 2 hours • Problem description 5W2H • Containment measures • Fishbone + 5Why first draft
Walkthrough 2 (Day2 Afternoon)
Given process → completed within 3h • PFMEA one line FM→FE→FC • Map CP one row • Six Elements of a Response Plan
QE empowerment training · QC→QE panoramic practice

## Slide 26
05
Quality management theoretical foundation
The “why” of QE

## Slide 27
Deming’s Fourteen Key Points (Excerpts related to QE)
① Establish constant purpose of improvement
⑤ Improve every process—the main battlefield of QE
⑥ On-the-job training—turn around and get training
⑨ Break down departmental walls - 8D cross-functional
⑪ Eliminate slogan-based management—require data and methods
⑬ Education and self-improvement - 90-day plan
Deming cycle = the theoretical origin of PDCA
QE empowerment training · QC→QE panoramic practice

## Slide 28
Juran Quality Trilogy
Quality planning (Planning)
• Identify customer needs • Design process meets needs • APQP/VOC/PFMEA all belong to this stage
Quality Control + Quality Improvement
• Control: SPC, CP, correction when process drifts • Improvement: breakthrough projects, DOE, Six Sigma
QE empowerment training · QC→QE panoramic practice

## Slide 29
Crosby · Taguchi · Six Sigma (Quick Facts)
Crosby: Free Quality, Zero Defects, Prevention, Cost of Measurement (COQ)
Taguchi: Quality is by design; robust parameter design; loss function (tolerance centrality)
Six Sigma: DMAIC structured improvement; black belt toolkit (regression, DOE, hypothesis testing)
Lean: Eliminate waste; combine with quality = Lean Six Sigma
QE doesn’t have to be a statistician, but you need to know “when to call for black belt support”
QE empowerment training · QC→QE panoramic practice

## Slide 30
Mapping of PDCA in QE work
Plan
Do a test run
Check data
Act standardization
QE empowerment training · QC→QE panoramic practice

## Slide 31
ISO 9001:2015 Seven Principles (QE Practice Points)
in principle | QE practice
Focus on customers | VOC, customer complaints, PPAP
leadership role | Decomposition of quality objectives
Everyone participates | Inspector feedback→PFMEA
process approach | Flow chart, turtle diagram
improve | 8D、Kaizen
evidence-based decision-making | SPC, data speak
relationship management | suppliers, customers
QE empowerment training · QC→QE panoramic practice

## Slide 32
Industry system increment (automotive/aviation)
IATF 16949: CSR, product safety, core tools, warranty data analysis
AS9100: Configuration management, first article identification FAI, key features, counterfeit parts
QEs in Tier1/2 must be familiar with the **Customer Special Requirements** Checklist
For details, see the think tank article: 2.1.2 IATF 16949 and AS9100
Theory is not a decoration - the review asks "What criteria do you base this control on?" You must be able to answer
QE empowerment training · QC→QE panoramic practice

## Slide 33
Cost of quality COQ (QE should be calculated)
category | Example | QE leverage
prevention | FMEA training, MSA | ↑ Often has the highest ROI
identification | Inspect labor and equipment | Optimal sampling
internal failure | scrap, rework | SPC + error proofing
external failure | Warranty, recall | Root cause + horizontal expansion
QE empowerment training · QC→QE panoramic practice

## Slide 34
06
Advanced Quality Planning APQP
QE node in the project

## Slide 35
APQP five stages (simplified)
plan
Product design and development
process design and development
feedback assessment
mass production
QE empowerment training · QC→QE panoramic practice

## Slide 36
VOC → special characteristics transfer chain
VOC: Customer voice, regulations, competitive products, warranty data
Special features: CC/SC/KCC/KPC - customer symbols are subject to CSR
Delivery: VOC → DFMEA → Drawings → PFMEA → CP → PPAP
QE Responsibilities: Ensure there are no breakpoints in the chain; changes in any link trigger downstream reviews
Think tank reference: 1.3.1 VOC, 8.3.x core tools
QE empowerment training · QC→QE panoramic practice

## Slide 37
APQP Core Tools and QE
tool | QE key actions
flow chart | Define process boundaries and handoffs
DFMEA | Design Risk → Verification Plan
PFMEA | Process FM/FC/Probe→Optimization
CP | Characteristics, methods, frequency, response
MSA | Gage GR&R precedes SPC
SPC | Process Stability and Capability
PPAP | Evidence package completeness and approval
QE empowerment training · QC→QE panoramic practice

## Slide 38
PFMEA seven-step method (QE must know)
Steps 1～4
• Planning and preparation • Structural analysis • Functional analysis • Failure analysis (FM/FE/FC)
Steps 5～7
• Risk analysis (AP=S×O×D) • Optimization measures • Documentation and Living FMEA
QE empowerment training · QC→QE panoramic practice

## Slide 39
Control Plan CP——QE’s Production Line Contract
CP answers three questions: What to control? How to control? What should I do if I lose control?
Items with AP=H in PFMEA must have executable control in CP
Six elements of response plan: stop, isolate, notify, handle, verify, record
CP, SOP, and inspection specification versions must be consistent among the three parties
Supporting courseware: Control Plan CP Training PPT (8.3.2)
QE empowerment training · QC→QE panoramic practice

## Slide 40
PPAP and QE
Submission level (common)
• Level 3: PSW + sample + complete support data • Contains PFMEA, CP, MSA, SPC, appearance approval, etc.
QE Audit Key Points
• Special features are consistent across packages • Quote data only if MSA is qualified • Trial production data support capability index
QE empowerment training · QC→QE panoramic practice

## Slide 41
Stage Gate Review (QE Checklist Excerpt)
node | QE must check
Gate 2 | DFMEA and prototype verification
Gate 3 | PFMEA/CP first version, MSA plan
Gate 4 | Trial production SPC, PPAP draft
Gate 5 | Mass production CP, Layered Audit
QE empowerment training · QC→QE panoramic practice

## Slide 42
07
problem solving
8D · 5Why · A3

## Slide 43
8D eight steps
D1 Team
D2 description
D3 containment
D4 root cause
D5 Countermeasures
D6 verification
D7 Prevention
D8 Commendation
QE empowerment training · QC→QE panoramic practice

## Slide 44
8D QE key points of each step
D2: 5W2H + samples/photos; avoid vague words such as "poor quality"
D3: Containment within 24 hours; rather large than small scope (batch/SN/in transit)
D4: Distinguish the causes of occurrence/outflow; verify the root cause (reproduce/eliminate)
D5: Countermeasures target root causes, not just additional inspections
D7: Horizontal expansion (similar products/processes/suppliers) + file update
D8: Team recognition – improving culture
QE empowerment training · QC→QE panoramic practice

## Slide 45
5Why and fish bones (cause and effect diagram)
5Why Rules
• Based on facts, ask questions one by one • To actionable root causes (processes/standards/training) • Avoid being stopped by “careless people”
Fishbone 4M1E
• People, Machine, Materials, Laws and Environments • Team co-creation, QE guidance does not do everything • Hypotheses require data validation (scatter plot/DOE)
QE empowerment training · QC→QE panoramic practice

## Slide 46
A3 Report (Lean Problem Solving)
One page: Background → Current Situation → Goals → Root Causes → Countermeasures → Plan → Follow-up
Suitable for internal improvement issues; 8D is still used for major customer complaints
A3 emphasizes Gemba and visual management
QE skills: compress complex problems into "one picture to explain clearly"
Think tank reference: 5.2.2 A3 Report and Issue Management
QE empowerment training · QC→QE panoramic practice

## Slide 47
Method Selection Guide
scene | Recommended method
Major quality accidents of customers | 8D + containment
Small internal duplication issues | A3 or simple 5Why
Unknown cause, multifactorial | DOE or regression
Failure mode system identification | FMEA
emergency containment | control plan response plan
QE empowerment training · QC→QE panoramic practice

## Slide 48
Calculation Case: Seal Leakage 8D (Abstract)
D4 root cause
• 5Why: Leakage → Seal groove size is out of tolerance → Tool wear → Tool change standard is not defined → CP has no process monitoring
D5～D7
• Countermeasures: Tool life management + groove diameter SPC • Verification: 32 piece capability Cpk≥1.33 • Horizontal: CP update for 3 coaxial production lines
QE empowerment training · QC→QE panoramic practice

## Slide 49
CAPA and recurrence prevention
Correction: Eliminate the cause of the nonconformity that has occurred
Prevention: Eliminate the causes of potential nonconformities
QE must prove: the measures are effective (compare data before and after)
Documentation: ECN updates FMEA/CP/SOP/training records
Validity review: 30/60/90 days tracking
QE empowerment training · QC→QE panoramic practice

## Slide 50
08
Seven QC Tools · QE Advanced Usage
From being able to use it to using it thoroughly

## Slide 51
① Checklist
QC: Tick record
QE: Design checklist structure → directly enter the database/hierarchical analysis
Key points: Field standardization, alignment with MES collection
Misunderstanding: Too many tables and no one can summarize them
QE empowerment training · QC→QE panoramic practice

## Slide 52
② Layer classification method
QC: Grouped by shift/machine
QE: Multi-dimensional intersection (machine × material batch × operator)
Key points: separate layers first and then draw to avoid mixed distribution
Think Tank: In-depth Interpretation Layer Method
QE empowerment training · QC→QE panoramic practice

## Slide 53
③Plato
QC: Counting defective items
QE: Define "items" and cost weights; focus on vital few
Key points: cumulative 80% principle + project approval
Misunderstanding: Inconsistent classification of categories leads to changes in conclusions
QE empowerment training · QC→QE panoramic practice

## Slide 54
④ Fishbone diagram
QC: Participate in brainstorming
QE: Guided Validation of Hypotheses; linked to 5Why/FMEA
Key Points: Cross-functional on-site development; avoid human responsibility
Supporting PPT: QC seven tool series
QE empowerment training · QC→QE panoramic practice

## Slide 55
⑤ Scatter chart
QC: See if it matters.
QE: correlation coefficient r, regression, residual analysis
Key points: The direction of cause and effect requires engineering judgment.
Application: Parameters vs Dimensions (Injection Temperature vs Shrinkage)
QE empowerment training · QC→QE panoramic practice

## Slide 56
⑥ Histogram
QC: Look at the distribution shape
QE: normality test, group interval selection, comparison with specifications
Key points: n is too small, don’t over-interpret it
Connection: pre-analysis of capability index
QE empowerment training · QC→QE panoramic practice

## Slide 57
⑦ Control chart
QC: Call the police
QE: Image selection (X̄-R/I-MR/p/np), reasonable subgroups, and difference rules
Key points: MSA first; out of control → response plan
Think Tank: 6.3.x SPC Series
QE empowerment training · QC→QE panoramic practice

## Slide 58
Seven tool combination boxing
Checklist + Level → Plato → Fishbone → Scatter → Control Chart Verification
QE project standard path: define → measure → analyze → improve → control
One-to-one correspondence with DMAIC stages
Exercise: Walk through 7 tools with the same data set
QE empowerment training · QC→QE panoramic practice

## Slide 59
09
Statistical Methods and Process Control
MSA · SPC · Capabilities · DOE

## Slide 60
MSA Measurement System Analysis (QE Access Control)
GR&R: %GRR < 10% excellent, 10~30% acceptable (the industry can be stricter)
Bias, linearity, stability - the entire life cycle of measuring tools
SPC data that has not passed MSA – a must-ask for review
Destruction Measurement: Nested GR&R
The MSA plan is linked to the CP "Evaluation/Measurement Technology" series
QE empowerment training · QC→QE panoramic practice

## Slide 61
Control Chart Selection (Getting Started)
data type | Commonly used pictures
meteringcontinuous | X̄-R、I-MR
Large metrology subgroup | X̄-s
Count defective product rate | p picture
Count defects | c/u diagram
QE empowerment training · QC→QE panoramic practice

## Slide 62
Cpk and Ppk
Cpk (potential capability)
• Within-group σ • See “how good it can be” when the process is under control • PPAP commonly used
Ppk (actual performance)
• Overall σ • Contains drift and anomalies • Mass production monitoring
QE empowerment training · QC→QE panoramic practice

## Slide 63
Cpk calculation example (summary)
Specification: 10.0 ± 0.2 mm; subgroup n=5, total 25 groups
Within group σ̂ = 0.04 → Cpk = min[(10.2-10.05),(10.05-9.8)]/(3×0.04) ≈ 1.25
Overall σ = 0.06 → Ppk ≈ 0.83 → Process instability or center deviation
QE action: first determine the heterostable process, and then talk about capabilities; if necessary, DOE finds factors
For details, see Think Tank: 6.3.2 Cpk/Ppk in-depth draft
QE empowerment training · QC→QE panoramic practice

## Slide 64
DOE Design of Experiments (Introduction to QE)
Purpose: Find significant factors and optimal parameters with minimal testing
2^k full factor, fractional factor, RSM response surface
Scenario: injection molding parameters, welding energy, cleaning time
Comparison with single-factor trial and error: efficiency and interaction effect discovery
Complex DOE can introduce Six Sigma black belts
QE empowerment training · QC→QE panoramic practice

## Slide 65
Western Electric Discrimination Rules (Excerpt)
rule | meaning
1 point over 3σ | special reasons
Same side as 9 o'clock | offset
6 points increment/decrement | trend
2/3 points exceed 2σ | early warning
QE empowerment training · QC→QE panoramic practice

## Slide 66
10
Inspection planning
QE design · QC execution

## Slide 67
IQC / IPQC / FQC / OQC planning logic
Risk orientation: Key characteristics are tightened; stable suppliers can reduce quantities
GB/T 2828.1 / ISO 2859-1: AQL, inspection level, transfer rules
Consistent with CP: If CP is written 100%, IQC cannot conduct random inspections secretly.
Exemption from inspection is not a lack of inspection - it is supplier process assurance + audit
Think Tank: 11.1.x Inspection Planning Series
QE empowerment training · QC→QE panoramic practice

## Slide 68
Sampling calculation (normal inspection example)
N batch | AQL | n samples | Ac/Re
500 | 1.0 | 50 | 1/2
1200 | 0.65 | 80 | 1/2
tighten | Same as AQL | n↑ | Ac↓
QE empowerment training · QC→QE panoramic practice

## Slide 69
Inspection tools and laboratories
Inspection tools
• Checking tool list, calibration cycle • Consistent with MSA • Limited sample management
laboratory
• OOS/OOT investigation • Method validation • Interfacing with LIMS (12.3.1)
QE empowerment training · QC→QE panoramic practice

## Slide 70
Right first order (RFT) and inspection efficiency
QE Goal: Source control reduces inspection load
FPY, RTY and inspection station bottleneck analysis
Poka-yoke is better than human inspection
Combining Lean SMED and OEE to see inspection downtime
Think Tank: 5.3.3 Right First Time and Source Control
QE empowerment training · QC→QE panoramic practice

## Slide 71
11
supplier quality
QE and SQE synergy

## Slide 72
Supplier quality management cycle
Choose: qualifications, process capabilities, quality system
Approval: PPAP/Prototype/Small batch
Monitoring: PPM, PPM Trends, Audits
Improvement: SCAR, 8D, on-site coaching
Exit: performance red lines, alternative suppliers
QE is often responsible for IQC standards and SCAR technical judgments
QE empowerment training · QC→QE panoramic practice

## Slide 73
Key points of second-party audit (QE can participate)
Dimensions | What to check
process | Is the PFMEA/CP consistent with the supplier?
Measurement | MSA, calibration
change | Notify customer mechanism
trace back | Batch/SN
QE empowerment training · QC→QE panoramic practice

## Slide 74
Calculation: Incoming PPM and SCAR
data
• 3-month PPM for a certain fastener = 850 • Main failure: Thread pass and stop gauge NG
QE+SQE
• SCAR requires supplier process capabilities • Update IQC and tighten to AQL 0.65 • PPM drops to 120 after 3 months
QE empowerment training · QC→QE panoramic practice

## Slide 75
PPAP Supplier Approval (QE Perspective)
Check PSW and commit element integrity
Transfer of special characteristics in supplier FMEA/CP
Material certification, sub-supplier list
Temporary approval (Waiver) must have a time limit and quantity
Think Tank: 8.3.3 PPAP Training PPT
QE empowerment training · QC→QE panoramic practice

## Slide 76
12
Customer Quality and Audit
Evidence based communication

## Slide 77
Customer Review Type
System Audit: ISO/IATF Compliance
Process audit: VDA 6.3, Layered Process Audit
Product review: Full size, functionality, durability
QE preparation: document index, mock questions and answers, evidence chain
Principle: Say less "should" and show more "records + data"
QE empowerment training · QC→QE panoramic practice

## Slide 78
Review high-frequency questions and QE responses
question | Qualified response elements
Is the CP consistent with the scene? | Version number+Layered Audit record
What should I do if my SPC is out of control? | Response plan example
When is the FMEA updated? | 4M Change/Invalidation Feedback
MSA expired? | Schedule + Report
QE empowerment training · QC→QE panoramic practice

## Slide 79
Customer complaint and warranty data analysis
Unify market failure codes with factory failure modes
Warranty PPM driven PFMEA optimization
Linked with **1.3.2 Satisfaction/NPS**, **1.3.3 Market Quality**
Major customer complaints: 24h preliminary report, 48h containment scope
QE is the "technical translator" between factories and customers
QE empowerment training · QC→QE panoramic practice

## Slide 80
PPAP Submit Dispute Resolution
Customers question
• Insufficient Cpk • Missing an MSA • Special features not noted
QE strategy
• Data transparency + improvement plan • Conditions for provisional approval • Don’t falsify data – red line
QE empowerment training · QC→QE panoramic practice

## Slide 81
Layered Audit Layered Audit
L1 monitor: press CP frequency
L2 Supervisor: Special Features and Response Plans
L3 Manager: System Effectiveness
QE Design Checklist and Defect Closed Loop
Audit findings→CAPA→File update
QE empowerment training · QC→QE panoramic practice

## Slide 82
13
Change · NCR · Documentation
QE’s system touchpoints

## Slide 83
4M Change Management
people
machine
material
Law
ring
trigger review
QE empowerment training · QC→QE panoramic practice

## Slide 84
ECN minimum package (QE takes the lead in checking)
Description and rationale for change
Impact assessment: products, processes, suppliers, customers
PFMEA/CP/SOP/Inspection Specification Difference Highlighting
Trial run/validation data
Training and cutover dates (Breakpoint Management 8.4.2)
QE empowerment training · QC→QE panoramic practice

## Slide 85
NCR Disposal Decision Tree (Simplified)
situation | Dispose
Small amount of NG in batch | Pick/Rework
Impact on safety/regulation | Scrap+Root Cause 8D
concession | Written approval + logo
recurring | CAPA+Management
QE empowerment training · QC→QE panoramic practice

## Slide 86
Documentation and version control
The only source of control: document control system or PLM
There is no "latest version" on site = serious non-compliance
QE maintenance quality level three document list
Record retention period: CSR normal ≥15 years (automobile)
Electronic Records: Audit Trail 12.1.2
QE empowerment training · QC→QE panoramic practice

## Slide 87
Traceability and recall preparation (QE responsibility)
daily
• SN/batch forward and reverse traceability • Shipping scanning rate ≥99.5%
crisis
• 24h simulated recall drill • Circle SN list for legal/PR
QE empowerment training · QC→QE panoramic practice

## Slide 88
14
digital quality
QMS/MES/Data

## Slide 89
Digital QE capabilities
Will define data requirements: what fields, what frequency, who is the owner
Understanding MES/QMS/LIMS Boundaries – Avoiding the Three Sets of Truths
Electronic CP, SPC automatic collection, NCR workflow
Dashboard: PPM, OEE, CPK Trends
Think Tank: 12.3.1 MES/QMS/LIMS Boundary
QE empowerment training · QC→QE panoramic practice

## Slide 90
System Boundaries (Quick Check)
system | master data
MES | Batch, process parameters, completion
LIMS | Inspection results and reports
QMS | NCR, CAPA, changes
QE empowerment training · QC→QE panoramic practice

## Slide 91
Predictive quality (look-ahead)
Parameter drift warning → intervene before deviation
Supplier performance forecast → advance review
AI visual inspection - QE defines defects and sampling inspection strategy
Digital twin (high-end scenario)
The foundation remains: MSA qualified data
QE empowerment training · QC→QE panoramic practice

## Slide 92
15
Soft skills and influence
Can be promoted even without rank

## Slide 93
Gemba genchigenbutsu
QE fixed weekly Gemba time - not in the office to pile reports
Observation: Standard work vs. reality; asking “Why is it done this way?”
Respect the scene; understand first and then improve
On-site with data: control charts, defective samples
QE empowerment training · QC→QE panoramic practice

## Slide 94
difficult conversation scene
scene | QE speaking principles
Request to stop line | Facts + CP + risks, give recovery conditions
Recommended supplier 8D | Data + contract, give deadline
refuse to accept concessions | Regulations/CSR, giving alternatives
Promote process improvement CP | Review risks + customer cases
QE empowerment training · QC→QE panoramic practice

## Slide 95
Reporting Structure (Pyramid)
Conclusion first: "It is recommended to suspend batch Bxxx because..."
Arguments: data, standards, scope of influence
Next steps: who, when, deliverables
8D client reporting is especially needed Executive Summary
QE empowerment training · QC→QE panoramic practice

## Slide 96
Mentorship and knowledge inheritance
Senior QE leads 1~2 QCs to turn around
Case library: Our factory’s real 8D/FMEA desensitized version
Reading Club: Think Tank Articles + Courseware Discussion
Certification: Internal QE L2/L3 Classification
QE empowerment training · QC→QE panoramic practice

## Slide 97
16
Practical workshops
Day 2～3 Comprehensive drill

## Slide 98
Workshop 1: PFMEA→CP linkage (3h)
Receive the real process in groups (desensitization)
Completed: 1 FM line + CP counterpart line + reaction plan
Mutual evaluation: Is AP=H under control? Is the reaction executable?
Commonly missed items in lecturer reviews
QE empowerment training · QC→QE panoramic practice

## Slide 99
Workshop 2: 8D Simulation (2h)
Given customer complaint scenario (including sample photos)
2h delivery: D1～D4 + containment range
Make up D5~D7 24 hours after class
Evaluation rubric: factuality, root cause depth, enforceability
QE empowerment training · QC→QE panoramic practice

## Slide 100
Workshop 3: Audit Simulation (2h)
Role Play: Auditor vs QE
Pump 5 high frequency questions
On-site adjustment CP/SPC/MSA records
Feedback: Is the chain of evidence complete?
QE empowerment training · QC→QE panoramic practice

## Slide 101
Exercise Rating Sheet (Excerpt)
item | Full marks | standard
Problem description | 15 | 5W2H Quantification
root cause | 25 | verification evidence
Countermeasures | 25 | Target the root cause
document | 20 | FMEA/CP updates
Express | 15 | Clear and concise
QE empowerment training · QC→QE panoramic practice

## Slide 102
Homework (90 days)
Select 1 production line to complete PFMEA/CP alignment
Dominant closure 1 up to 8D (including lateral expansion)
Complete 1 supplier or internal process audit
Submit monthly turnaround diary to instructor
QE empowerment training · QC→QE panoramic practice

## Slide 103
17
90 Day Turnaround Plan
Executable and acceptable

## Slide 104
90 day milestone
stage | Target | acceptance
0～30 days | Tool remedial lessons + follow-up projects | Pass L2 test
31～60 days | Standalone CP/8D node | 1 approved CP
61～90 days | APQP/Audit Participation | Instructor’s signature L2
QE empowerment training · QC→QE panoramic practice

## Slide 105
Week 1～4 Daily study suggestions
W1: QC vs QE roles + seven tools review
W2: PFMEA/CP courseware + mapping exercise
W3: MSA/SPC computer (Minitab/JMP)
W4: 8D template + factory case reading
1h study + 1h onsite every day
QE empowerment training · QC→QE panoramic practice

## Slide 106
Recommended Think Tank Learning Path
13.2.1 Job Competencies (this article)
8.3.1 PFMEA · 8.3.2 CP · 8.3.3 PPAP
5.2.1 8D · 5.2.2 A3 · 6.3.x SPC
11.1.x Inspection · 9.3.2 Traceability · 2.1.2 IATF
Database download supporting PPT and templates
QE empowerment training · QC→QE panoramic practice

## Slide 107
QE Turn Around Checklist (Final Draft)
# | Check items | □
1 | Able to independently interpret one line of PFMEA to one line of CP | 
2 | Can dominate 8D D1～D7 | 
3 | Can construct X̄-R and determine its difference | 
4 | Able to answer 10 frequently asked questions in customer reviews | 
5 | Complete 90-day project log | 
QE empowerment training · QC→QE panoramic practice

## Slide 108
18
Common misunderstandings
Turn around and avoid the pit

## Slide 109
Top ten misunderstandings
Misunderstanding | Countermeasures
Still at the inspection post | RACI+KPI adjustment
Only additional inspections will be done | Root cause + process control
FMEA fill out and discard | Living FMEA
CP copy paste | Create new process by process
Ignore MSA | GR&R first, then SPC
8D Pass the blame to others | System reasons
Afraid of line interruption | Response plan pre-alignment
The file version is messed up | Document control+ECN
Not collaborating with suppliers | SQE United
Not learning standards | CSR Checklist
QE empowerment training · QC→QE panoramic practice

## Slide 110
A word from a quality manager to QE
"Your value is not to find more bad things, but to make them no longer meaningful."
Inspection is the last line of defense; engineering prevention is the main business of QE
Take 90 days to prove: you deserve a seat at the PFMEA meeting
QE empowerment training · QC→QE panoramic practice

## Slide 111
QE panoramic capability map - five-question self-examination
🎯
who I am?
📋
Control what?
🔧
How to control?
📊
Is the data trustworthy?
🚀
How to improve?
summary
QC → QE is a career transition: from "gatekeeping" to "designing gatekeeping solutions and eliminating risks." This courseware covers roles, theories, APQP tools, problem solving, statistics, supply chain, customers and digitalization - 2-3 days of intensive training + 90 days of project-based coaching are recommended. Next step: receive the 90-day plan template, select a mentor and the first pilot production line, and complete the first PFMEA meeting speech this week.
QE empowerment training · QC→QE panoramic practice

## Slide 112
Q & A
Supporting think tank: Job Competency Model 13.2.1 · PFMEA/CP/PPAP courseware · QC seven tool series · qtank.org

## Slide 113
thanks for listening
qtank.org
QTank
qtank.org