## Slide 1
SPC statistical process control practical training (including Minitab operation)
From basic statistics to control chart application, process capability analysis (CPK/PPK), exception handling, with MINITAB practical videos and practice data
QTank
Knowledge No. 6.3.1 · Control Chart Selection and Discrimination
qtank.org

## Slide 2
CONTENTS
Table of contents
  SPC basics and statistical principles
  Control Chart Principles and Applications
  Process capability analysis in practice
  Process exception analysis and handling
  Minitab practical drill
  Comprehensive case practice

## Slide 3
Part.
SPC basics and statistical principles
01

## Slide 4
statistical process control definition
SPC is a method of real-time monitoring of the production process through statistical analysis technology, aiming to identify abnormal variations and take corrective measures to ensure that the process is stable and controlled.
Quality Prevention Tools
The core role of SPC is to shift from passive detection to active prevention, discover potential problems in advance through control charts and other tools, and reduce the production of defective products and quality costs.
process capability quantification
Quantify process capabilities by calculating indicators such as CPK and PPK to provide data support for quality improvement and help companies achieve Six Sigma management levels.
decision support system
SPC data provides management with an objective basis for decision-making, avoiding judgment based on experience and realizing a data-driven quality management model.
Basics of continuous improvement
SPC is a key tool in the Check phase of the PDCA cycle, providing a visual feedback mechanism for continuous improvement.
SPC definition and core role
01
02
03
04
05

## Slide 5
Identify improvement opportunities through variation analysis to improve process stability and capability index
common cause variation
Random fluctuations inherent process variation not attributable to a specific cause
Adjust equipment parameters Optimize process parameters
1
Use error-proofing techniques to reduce human intervention
2
trend variation
Progressive Offset Tool Wear Material Aging
Regular equipment maintenance Establish replacement standards
1
SPC Monitoring Predictive Maintenance
2
special cause variation
Abnormal fluctuations with “identifiable causes” requiring immediate intervention
5Why analysis method Fishbone diagram analysis
1
Implement control charts Establish alarm mechanism
2
periodic variation
Seasonal Fluctuations Shift Differences Environmental Cycles
Time Series Analysis Spectral Analysis
1
Adjust control limits stratified analysis
2
Analysis of process variation types and causes
Improvement strategies: root cause analysis
Improvement Strategies: Pattern Recognition
Improvement strategies: process optimization
Improvement strategies: preventive maintenance

## Slide 6
Normal distribution and basic statistics
Normal distribution characteristics
The bell-shaped symmetrical curve is completely determined by the mean μ and the standard deviation σ, covering the practical application scenarios of 68-95-99.7% of the rules of thumb.
01
central limit theorem
Regardless of the original distribution shape, the sample mean distribution approaches a normal distribution as the sample size increases, which is the theoretical basis of control charts.
02
Statistics calculation
Describe in detail the calculation formulas for statistics such as mean, range, moving range, standard deviation and their implementation paths in Minitab.
03
Distribution pattern diagnosis
Verify the normality of the data through normal probability plots, Anderson-Darling tests and other methods to guide the selection of subsequent analysis methods.
04
Non-normal data processing
For skewed/kurtotic data, we introduce normalization processing methods such as Box-Cox transformation and Johnson transformation and the key points of Minitab operation.
05
Prerequisites for process capability analysis
Emphasis is placed on the impact of the three prerequisites of normality testing, stability verification, and data independence on the accuracy of process capability analysis.
06

## Slide 7
Part.
Control Chart Principles and Applications
02

## Slide 8
Control chart types and selection criteria
A normality test needs to be performed before selecting a control chart. Non-normal data needs to be converted or a non-parametric control chart should be selected.
Data distribution analysis
It is suitable for continuous variable data, such as size, weight, temperature, etc., and is preferred when the data obeys a normal distribution and the sample size is small.
Measurement type control chart
The I-MR chart is suitable for short-term process fluctuation analysis, and the Xbar-R chart is suitable for long-term process stability monitoring.
Matching process characteristics
It is suitable for discrete variable data, such as number of defects, defective product rate, etc. It can be divided into P chart, U chart and C chart according to the data type.
Count control chart
For large samples, it is recommended to use the Xbar-S chart instead of the Xbar-R chart, while for small samples, the I-MR chart is preferred.
Sample size considerations
When there are multiple relevant quality characteristics, multiple control methods such as T² control charts need to be used.
multivariable control chart

## Slide 9
  Advantages of Xbar-R graph: Suitable for small sample sizes, capable of simultaneously monitoring process center and discreteness, simple calculation, and low implementation cost.
  Xbar-S chart applicability: Suitable for large sample sizes, using standard deviation instead of range for more accurate variability monitoring.
  I-MR chart features: Suitable for single measurement value or high-cost detection, monitoring adjacent sample fluctuations through moving range.
  The difference between P chart and C chart: Chart P monitors the rate of defective products, chart C monitors the number of defects per unit product, and is suitable for different discrete data scenarios.
  Control chart selection principles: Select the appropriate control chart type based on data type, sample size, testing costs, and sources of process fluctuations.
  Practical application cases: The Xbar-R chart is used for battery core winding tightness testing, and the I-MR chart is used for steel composition analysis in spectroscopic laboratories.
Control chart type | Applicable scenarios | Main features
Xbar-R plot | The sample size of the subgroup is small (2-9), and both the mean and variability need to be monitored | The calculation is simple, the implementation cost is low, and it can reflect the process center and discrete degree.
Xbar-S diagram | Subgroup sample size is large (≥10) and variability needs to be monitored more accurately | Use standard deviation instead of range, suitable for large sample sizes
I-MR chart | Single measurement values ​​that cannot be grouped, such as liquids, gases or homogeneously mixed materials | Monitor adjacent sample fluctuations through moving range, suitable for high-cost or time-consuming inspections
P picture | Monitor the rate of defective products, suitable for discrete data | Visually display changes in the rate of unqualified products, suitable for quality monitoring
C picture | Monitor the number of product defects per unit, suitable for scenarios where the number of defects is fixed | Directly reflects changes in the number of defects and is suitable for production processes with a fixed number of defects.
Metering type control chart (Xbar-R, I-MR)

## Slide 10
P picture application scenarios
To monitor the proportion of unqualified products, the sample size is required to be fixed or change no more than ±25%, and the control limits are in a zigzag shape.
The defect number control chart requires the inspection area to be fixed, such as the welding defects of each circuit board.
When the actual variation is greater than the theoretical variation, the Laney P' or U' chart needs to be used to adjust the control limits.
Count type control chart (P, U, C chart)
Applicable conditions for Figure C
Overdispersion
Features of U diagram
Tracking the number of unit defects is suitable for situations where the sample size fluctuates greatly, and the standardized defect rate needs to be calculated.
The P chart is based on the binomial distribution, and the U/C chart is based on the Poisson distribution, and the distribution assumptions need to be verified.
Statistics → Control Chart → Attribute Control Chart, you need to distinguish between "defect" and "defective product" data types.
Binomial distribution and Poisson distribution
Minitab implementation path

## Slide 11
criteria
contrast
fact
Eight criteria for judging differences in control charts
Principle 1
Point outside control limits: When a data point falls outside the control limits, it indicates special cause variation in the process.
Principle 2
7 consecutive points on the same side: 7 consecutive points on the same side of the center line, indicating a shift in the process mean.
Principle 3
Continuous rise/fall: 6 consecutive points show a monotonic rising or falling trend, indicating that there is drift in the process.
01
02
03

## Slide 12
Part.
Process capability analysis in practice
03

## Slide 13
Concept analysis of Cp/Cpk and Pp/Ppk
Cp/Cpk definition
Cp (process capability index) describes the potential ability of a process to meet product quality specification requirements, and it takes into account the inherent variation of the process; Cpk (process capability index considers deviation) further considers the deviation between the process mean and the specification center value, and is a more comprehensive process capability evaluation index.
Pp/Ppk definition
The difference between Cp and Pp
Pp (process performance index) is similar to Cp, but it is calculated based on long-term data and reflects the actual performance of the process over a longer period of time; Ppk (process performance index considering offset) also considers the offset of the process mean and the specification center value, and is an important indicator for evaluating the long-term stability of the process.
The main difference between Cp and Pp is that the data basis is different. Cp is based on short-term data, reflecting the potential capability of the process under control; while Pp is based on long-term data, taking into account the actual performance of the process under the influence of various factors, and can better reflect the true situation of the process.
1
2
3

## Slide 14
The difference between Cpk and Ppk
Cp/Cpk is mainly used to evaluate whether a new or improved process meets product quality requirements and helps determine whether the process needs further adjustment or optimization. At the same time, they are also important indicators in process audit and certification, used to prove that the process has the ability to stably produce qualified products.
Cp/Cpk application scenarios
Pp/Ppk application scenarios
Pp/Ppk is more suitable for evaluating the long-term stability and performance of existing processes and helping to identify possible long-term problems or trends in the process. By regularly calculating the Pp/Ppk value, you can monitor the performance changes of the process, discover and take measures to prevent potential quality problems in a timely manner.
Cpk and Ppk are similar in accounting for offsets, but have different data bases. Cpk is based on short-term data and is used to evaluate the ability of the process in a controlled and stable state; Ppk is based on long-term data and can better reflect the performance of the process in actual operation, including possible offsets and fluctuations.
Concept analysis of Cp/Cpk and Pp/Ppk

## Slide 15
Minitab operations
Interpretation of results
Indicator calculation
stage
data collection
Parameter calculation
Capability analysis
Report output
Process capability calculation and result interpretation
Cp=(USL-LSL)/6σ, reflecting the potential capability of the process
Cp calculation
Cp standard
Enter the data column in Minitab by Stat>QualityTools>CapabilityAnalysis
data entry
Cpk=min(USL-μ,μ-LSL)/3σ, reflects the actual process capability
Cpk calculation
Cpk standard
Analyze normal probability plots, histograms and control charts to determine process stability
Graphic interpretation

## Slide 16
Improvement measures
Data anomaly
Cpk is low
Insufficient Cp
Optimize control strategy:
Analyze key parameters through Minitab and adjust the process window to make the process capability index reach the target value.
root cause analysis
Revise the operation standard book based on the process capability analysis results to ensure that the process parameters are reasonable and controllable.
Problems with excessive variation:
Use variance analysis to locate the source of variation, and reduce process fluctuations through DOE experimental optimization.
Improve data quality:
Regularly calibrate the measurement system to eliminate the impact of MSA errors on process capability analysis.
Use Minitab to test the normality of the data, and then calculate the capability index after eliminating outliers.
Parameter offset problem:
Identify significant shifts in key parameters through hypothesis testing and adjust process center values ​​accordingly.
Directions for improvement of insufficient abilities
Adjust parameters:
Update criteria:
Calibration equipment:
Filter data:

## Slide 17
Part.
Process exception analysis and handling
04

## Slide 18
Special cause identification method
control chart method
Use control charts to monitor process data in real time, and identify special causes by observing whether data points exceed control limits or present non-random distribution, such as points out of bounds, several consecutive points on the same side of the center line, trend changes, etc.
Cause and Effect Diagram (Fishbone Diagram) Method
By drawing a cause-and-effect diagram, the problem is taken as the result, and the possible causes are analyzed from multiple aspects such as people, machines, materials, methods, and environment, and the special reasons for the abnormal process are found out one by one.
Hypothesis testing method
Based on statistical principles, hypothesis testing is performed on process data, such as t-test, variance analysis, etc., and by comparing the differences between actual data and theoretical distribution or expected values, it is determined whether there are abnormal fluctuations caused by special reasons.

## Slide 19
Special cause identification method
Scatter plot method
Use a scatter plot to show the relationship between two variables. By observing the distribution shape and trend of the scatter points, you can determine whether there are correlation changes caused by special reasons, and then identify the cause of the anomaly.
regression analysis
By establishing a regression model, we analyze the relationship between independent variables and dependent variables, and use the difference between model predicted values ​​and actual values ​​to identify whether there are abnormal fluctuations caused by special reasons and further locate the causes.
experimental design method
By designing reasonable experimental plans, making planned changes to process parameters and observing changes in process output, we can identify special causes that have a significant impact on process stability and provide the basis for subsequent improvements.

## Slide 20
Exception root cause analysis tool
By continuously asking "why" at five levels, we can penetrate the superficial phenomena and get to the root causes. We need to cooperate with on-site verification to prevent logical deviations.
01
Use Minitab's graphical tools to build a cause-and-effect analysis framework that includes six dimensions: human, machine, material, method, environment, and measurement.
02
Failure Modes and Effects Analysis (FMEA)
Quantitatively evaluate the severity, frequency and detection of potential failure modes, and calculate the risk priority number RPN to guide the direction of improvement.
03
Flexibly use statistical methods such as two-sample t-test, analysis of variance (ANOVA), and chi-square test to verify root cause hypotheses.
04
Establish a mathematical model of key parameters and quality characteristics through response surface method (RSM) to find the optimal parameter combination window.
05
Fishbone diagram (characteristic factor diagram) drawing
Three-dimensional parameter optimization design
Hypothesis testing toolset
5Why analysis method in practice

## Slide 21
Anomaly analysis
prevention mechanism
Improve FMEA analysis to identify potential failure modes and impacts in advance.
Identify abnormal data points, analyze root causes, and develop targeted improvement plans.
Establish a quick response mechanism to adjust process parameters in a timely manner to prevent problems from expanding.
01
Optimize control plans, improve work instructions, and reduce mutation risks.
02
Strengthen personnel training, improve operational standardization, and reduce human errors.
03
Implement continuous monitoring to verify the effectiveness of measures and ensure process stability.
04
Establish an SPC early warning system to monitor key quality characteristics in real time.
01
Regularly review control charts to identify trend changes and intervene in advance.
02
Standardize best practices and form a library of error-proofing technical documents.
03
Carry out process capability research and continuously optimize process parameter settings.
04
system
technology
data
personnel
Corrective actions and preventive mechanisms

## Slide 22
Part.
Minitab practical drill
05

## Slide 23
Data import and preprocessing skills
Data format conversion and standardization
According to the analysis needs, the necessary format conversion is performed on the data, such as date format, text format, etc. At the same time, the data is standardized to eliminate the dimensional impact, so that different variables are comparable and the accuracy of the analysis is improved.
Data cleaning and outlier processing
Use Minitab's data filtering and sorting functions to identify and process outliers, missing values, and duplicate values ​​in the data, and ensure data quality through replacement, deletion, or interpolation, laying the foundation for subsequent analysis.
Data import method selection
According to the data source and format, choose the appropriate data import method, such as importing from Excel, CSV, TXT and other files, or directly connecting to the database to import data to ensure that the data enters the Minitab worksheet accurately.

## Slide 24
Master the data splitting function in Minitab to split a column of data into multiple columns according to specific rules to facilitate subsequent analysis. At the same time, use the data merging function to merge multiple data tables according to common fields to achieve data integration and association.
Data import and preprocessing skills
Data sorting and merging techniques
According to the purpose of analysis, flexibly use Minitab's data filtering function to extract data subsets that meet specific conditions. In addition, master data sampling methods, such as simple random sampling, stratified sampling, etc., to extract representative samples from a large amount of data for analysis.
Data screening and sampling methods
In order to improve the efficiency of data preprocessing, you can write Minitab scripts to automate data import, cleaning, conversion and other steps to reduce repeated operations. At the same time, standardize data preprocessing through scripts to ensure consistent data quality each time processed.
Data preprocessing automation script

## Slide 25
Control chart automatic generation operation
Select the subgroup capacity in "Statistics-Control Chart-Variable Control Chart of Subgroup", automatically calculate CL/UCL/LCL and mark the exceeding limit points.
Mean-Range Control Chart (Xbar-R)
For continuous production scenarios, real-time monitoring charts are generated through "single-value variable control charts", and the process offset alarm function is linked.
Individual Value-Moving Range Chart (I-MR)
Through the "Multivariable Control Chart" module, joint monitoring of relevant parameters is realized, and T² statistics are used to detect multivariate process anomalies.
multivariable control chart
Set 8 major Western Electric rules in "Options-Inspection" to automatically mark abnormal patterns such as continuous 7-point rise/periodic fluctuation.
Custom rule configuration
Set the sample size and number of defects in the "Attribute Control Chart" to automatically calculate proportional control limits and identify special cause variation patterns.
Defective product rate P chart

## Slide 26
Normal Process Capability Analysis
Short term/long term capability comparison
Target value deviation analysis
Binomial Distribution Power Analysis
Non-normal data transformation
Process capability analysis implementation
Use "Statistics-Quality Tools-Capability Analysis-Normal" to calculate Cp/Cpk/Pp/Ppk, and output a comparison report between potential capabilities and actual capabilities.
Normalize skewed data through "Johnson transformation" or "Box-Cox transformation", and select the optimal fitting distribution in the "Individual Distribution Identification".
For the defective product rate data, "binary capability analysis" is used to calculate the Z benchmark value and confidence interval, and visualize the DPU/DPO index.
Distinguish between σwithin and σoverall through "between/within group" variance decomposition to evaluate process stability and room for improvement.
In the "Capability Six Pack", the offset between the process center and the specification center is displayed, and the Sigma level and DPMO value are calculated.

## Slide 27
Dynamic chart interaction
Real-time Kanban configuration
Data export standardization
3D process capability diagram
Customized report generation
Results visualization and report output
Supports click-drilling on control charts to view subgroup details, and the right-click menu can add reference lines/adjust axis ranges/switch display dimensions.
Use the "Report-Create Report" function to combine control chart/capability analysis/histogram and other elements to automatically generate PDF/HTML format documents.
The spatial distribution of LSL/USL/Target is displayed in the "Graphic-3D Scatter Plot" to visually present the risk of process deviation.
Save key control charts as "Preferences-Dashboard" to realize automatic refresh of multi-indicator monitoring views and email alerts.
Supports exporting analysis results in ASQ/ISO format, including complete metadata annotations and calculation process traceability information.

## Slide 28
Part.
Comprehensive case practice
06

## Slide 29
Manufacturing process control case
Injection molding parameter optimization
Monitor key parameters such as melt temperature and injection pressure through SPC to identify the root causes of process variation, analyze the Cp/Cpk value with Minitab, and optimize the process window to reduce product warpage defects.
Welding strength stability analysis
Collect weld strength data, use control charts to determine whether the process is under control, develop a welding gun maintenance plan for special causes of variation, and improve welding consistency.
Assembly line dimensional tolerance monitoring
Implement Xbar-R chart real-time monitoring of key assembly dimensions, conduct normality testing and process capability analysis through Minitab, and reduce the rework rate by more than 15%.
Improved coating thickness uniformity
Based on the histogram and Pareto chart, the nozzle wear problem of the spraying equipment was identified, and the thickness CPK was increased from 0.8 to 1.33 after adjusting the air pressure parameters.
Reduced defective rate of stamping parts
Through hierarchical analysis of defect types, the locked mold gap is the key factor. After optimization using DOE experiments, the defective rate was reduced from 5% to 0.7%.

## Slide 30
data collection
Teamwork
process capability
Carry out SPC data collection training, guide team members to formulate measurement plans, determine reasonable sampling frequencies, and master the identification methods of special causes and common causes.
Conduct process capability analysis training for the current production process, master CP/CPK calculation and interpretation methods, and learn to use control charts to identify sources of process variation.
Special SPC training: organize practical training such as control chart interpretation and process stability analysis to improve the team's sensitivity and response speed to variation signals
Improvement measures: Skill strengthening
Minitab application: Use Minitab for data entry and outlier screening, and establish standardized data collection templates to ensure the stability of the measurement system
Automated analysis: Use Minitab macro commands to automatically generate process capability reports and establish a real-time monitoring system to reduce manual analysis errors
Minitab collaboration: Establish a shared analysis template library to achieve real-time synchronization of control chart data and multi-position collaborative analysis through the central database
Improvement measures: system optimization
Continuous improvement project implementation

## Slide 31
Practice data analysis after class
Thread aperture stability: 300 sets of aperture measurement data are provided, and students are required to complete stability analysis, process capability calculation and inference of root causes of abnormal points.
Case 1
Case 2
Case 3
Case 4
Case 5
Case 6
Battery voltage consistency: Contains voltage test data of 5 production lines. It is required to use box plots to compare differences in production lines and design improvement plans.
Packaging weight compliance: simulate FDA audit scenarios and generate reports based on 2,000 pieces of weight data, including trend analysis, traceability of out-of-standard batches and corrective measures.
Heat treatment hardness distribution: Different heat hardness values ​​are given to guide students to complete normality conversion, control weight limit calculation and long-term process performance evaluation.
Stamping speed impact analysis: including paired data of speed parameters and dimensional deviations, practicing regression analysis and interaction diagram drawing.
Cleanliness testing data: For particle count data, teachers use Poisson distribution control charts to monitor and formulate cleaning standard optimization suggestions.

## Slide 32
thanks for listening
qtank.org
QTank
qtank.org