## Slide 1
First Article Inspection (FAI)
Practical Training
Inspect one product · intercept a batch's quality risk
QTank
Knowledge Code 11.1.1 · IQC/IPQC/FQC/OQC Planning
qtank.org

## Slide 2
Training Objectives
After training, able to answer: When? Who? What to inspect? What if non-conforming?
Clarify two levels: production first article confirmation vs. new product FAI Report
Master seven mandatory FAI trigger scenarios; document in CP/work instructions
Implement self/cross/special three-inspection system and eight-step standard process
Design inspection items and judgment rules per CP/special characteristics/drawings/historical defects
Connect FAI with process control, SPC, PPAP; build first-pass yield improvement mechanism
First Article Inspection (FAI) Practical Training

## Slide 3
01
Why First Article Inspection Is Mandatory
First Gate Before Batch Production

## Slide 4
Two Levels — Do Not Confuse
Production First Article Confirmation
• After line/mold/material/personnel change • Focus: 'Can this batch be run?' • Starting point of routine in-process inspection
New Product First Article (FAI Report)
• After new product or major change • Full-dimension / full-performance inspection report • One of core PPAP submission attachments
First Article Inspection (FAI) Practical Training

## Slide 5
Core Question FAI Answers
Under current Man/Machine/Material/Method/Environment/Measurement conditions, can we consistently produce conforming product?
Cost leverage: intercepts 'batch errors' at cost of inspecting one unit
Change-sensitive: quality variation often from condition changes; FAI is first exposure sample
Compliance: IATF 16949, GJB 9001 etc. explicitly require and retain records
Positioning: confirm 'process readiness' — not 'one more inspection step'
First Article Inspection (FAI) Practical Training

## Slide 6
02
When FAI Is Mandatory
Seven Triggers + Document in Files

## Slide 7
Seven Mandatory FAI Scenarios
Scenario | Key Points
Changeover / Line Change | First article mandatory after product switch or line adjustment
Mold/Tool Change | Mold/tool/fixture replacement or readjustment
Material Change | Raw/auxiliary material batch change, especially affecting key characteristics
Personnel Change | Operator/inspector/setup technician change
Equipment Adjustment/Repair | Major repair, parameter adjustment, restart after shutdown
Process Change | Parameter, method, or environmental condition change
Shift Start | Daily shift start, first article after long holiday restart
First Article Inspection (FAI) Practical Training

## Slide 8
Trigger mechanism must be documented
Write in Control Plan (CP) and work instructions: what condition → who initiates → what to inspect → who judges
Use first article confirmation form for traceability — eliminate 'self-discipline is enough'
Where possible, set FAI release in MES: batch cannot start without confirmed pass
Quantity: typically 1–3 units; 3 for high-risk processes (cover multiple stations)
Scope: full key characteristic coverage — dimensions, appearance, performance, assembly, packaging
First Article Inspection (FAI) Practical Training

## Slide 9
03
How to Do It
Three-Inspection · Eight-Step Process · Three Record Elements

## Slide 10
Three-Inspection System
Self-inspection (operator)
Cross-inspection (team)
Special inspection (inspector release)
First Article Inspection (FAI) Practical Training

## Slide 11
Roles & Authority Matrix
Role | Responsibilities | Authority
Operator | First article self-inspection, record anomalies | No release authority
Team Leader | Cross-inspection, organize root cause analysis | No release authority
Inspector | Special inspection, final judgment | Authority to release / hold
Quality Engineer | Anomaly handling, change review | Authority to adjust plan
First Article Inspection (FAI) Practical Training

## Slide 12
Three Elements of First Article Records
Inspection items and measured values (not just writing 'Pass')
Inspection basis and gauge ID (traceable)
Judgment conclusion and signature (with timestamp)
Retention per customer and system requirements (automotive often covers product lifecycle)
Records without measured values or gauge IDs = no inspection done
First Article Inspection (FAI) Practical Training

## Slide 13
Eight-Step Standard Process
① Trigger Confirmation
② Trial First Article
③ Self-inspection
④ Cross-inspection
⑤ Special Inspection Judgment
⑥ Release Identification
⑦ Non-conformance Closure
⑧ Archive in System
First Article Inspection (FAI) Practical Training

## Slide 14
Process must be 'short and strict'
No step skipped: any failure blocks batch production
Keep wait time per step in minutes — avoid FAI becoming delivery bottleneck
Non-conformance: isolate → analyze → re-trial → re-inspect pass before resuming
Strictly prohibit 'tweak and concession release' fake first articles
After pass: mark first article and complete system entry
First Article Inspection (FAI) Practical Training

## Slide 15
04
What to Inspect, How to Judge
Item Design & Appearance Criteria

## Slide 16
Five Sources of Inspection Items
Not inspector 'by experience' ad-hoc item selection
Product and process characteristics in Control Plan (CP)
Special characteristics list: CC/SC must be fully covered
Drawings and specs: dimensions, tolerances, material, surface treatment
Historical defects: prioritize confirmation on first article for similar products
First article items in Customer Specific Requirements (CSR)
First Article Inspection (FAI) Practical Training

## Slide 17
How to Handle Non-conforming First Articles
Must Do
• Stop batch production immediately • Isolate / identify / review • 4M1E root cause analysis • Re-trial and re-inspect • Document causes and actions
Must Not Do
• Verbal 'close enough' to start line • Change records only, not process • Concession first article straight to mass production • Special inspection only, no self/cross inspection • Write 'Pass' only without measured values
First Article Inspection (FAI) Practical Training

## Slide 18
Appearance First Article Judgment Criteria
Limit samples: pass upper limit and fail lower limit for on-site comparison
Defect atlas: photo archive of common appearance defects for training and judgment
Consistency check: periodic independent judgment of same sample set, calibrate disagreements with Kappa
Update criteria documents and limit samples with product changes, mark version
Prevent judgment disputes from mixing old and new standards
First Article Inspection (FAI) Practical Training

## Slide 19
New Product First Article & Full-Dimension Inspection Report
Measure and record all drawing dimensions and characteristics item by item
Include Cpk/Ppk data when process capability is required
Archive material reports, performance tests, appearance limit samples together
Report is core PPAP attachment (e.g., PSW)
No batch supply before customer approval
First Article Inspection (FAI) Practical Training

## Slide 20
05
Integration with Process Control
Correct Start + Stable Process

## Slide 21
FAI is not the end — it is the start
First article pass ≠ entire batch stable
Afterward rely on CP in-process inspection, SPC monitoring, mistake-proofing to eliminate human error
FAI manages 'correct start'; process control manages 'process stability'
FAI data: adjustment count, non-conformance items, cause distribution → monthly analysis
Frequent FAI failures → drive changeover standardization/SMED/update FMEA·CP
First Article Inspection (FAI) Practical Training

## Slide 22
Digital FAI (Optional Advanced)
Auto-trigger FAI task on condition change
Mobile entry of inspection results
Auto-hold batch on non-conformance
Data feeds quality dashboard and first-pass yield metrics
Prerequisite remains: clear logic, defined roles — digitalization is not the goal
First Article Inspection (FAI) Practical Training

## Slide 23
06
Pitfalls & Implementation
Five Pitfalls · Five-Step Path · Three Audit Questions

## Slide 24
Five Common Pitfalls
Pitfall | Correct Understanding
Inspector's job only | Must include self + cross + special inspection
First article pass = entire batch pass | Process control still needed after correct start
Writing 'Pass' is enough | Must have measured values and gauge IDs
FAI only on changeover | Material/personnel/repair/restart also require FAI
Non-conformance fixed and released | Must re-trial and re-inspect
First Article Inspection (FAI) Practical Training

## Slide 25
Five-Step Implementation Path
Step | Action | Key Output
1 | Map triggers and current state | Trigger checklist, gap analysis
2 | Define three-inspection and process | Process documents, roles matrix
3 | Design items per CP | Item list, first article confirmation form
4 | Training and trial run | Training records, issue list
5 | Monitoring and continuous improvement | First-pass yield, monthly analysis
First Article Inspection (FAI) Practical Training

## Slide 26
Three Self-Audit Questions
Are trigger conditions documented?
Can first article records trace to specific batch and gauge?
Did non-conforming first article complete isolate-analyze-reverify loop?
Internal/external audit hot spots: triggers, record completeness, non-conformance handling
Doing it well is both quality assurance and compliance 'must-answer'
First Article Inspection (FAI) Practical Training

## Slide 27
One-Line Summary
Use one product's inspection cost to intercept a batch's quality risk
Intercept 'done wrong' before 'done too much'
Documented triggers · Clear three-inspection · Complete items · Traceable records · Data feedback
FAI is no longer a signature exercise — it is one of the highest-ROI quality gates
First Article Inspection (FAI) Practical Training

## Slide 28
Q & A
Related article: id=275 First Article Inspection (FAI) Practical Guide · Knowledge Code 11.1.1

## Slide 29
Thank You
qtank.org
QTank
qtank.org