## Slide 1
Five-Step In-Plant Logistics Quality Control
Turn Blind Spots into Quality Defense Lines
Damage, wrong parts, mixed batches every year? Handling·Storage·Delivery·Packaging·Labeling in closed loop
QTank
Knowledge Code 7.4.2 · Layout & Logistics Quality
qtank.org

## Slide 2
CONTENTS
Course Outline
From"Blind Spots"to Quality Defense — Five-Step System Overview
01
Current State Insight · Invisible"Transport Fleet"
Why In-Plant Logistics Is Quality Management's"Blind Spots"
P.03
02
Four Killers · Know the Enemy Before Acting
Handling Damage · Wrong Pick/Delivery · Mixed Batch / Broken Traceability · Storage Degradation
P.05
03
Five-Step Framework · Manage Logistics as a Process Step
Handling → Storage → Delivery → Packaging & Labeling → Measurement Closed Loop
P.07
04
Handling + Storage · Secure the First Two Gates
Material Characteristic Matching · Location-Based FIFO · Environmental Compliance
P.09
05
Delivery + Packaging + Closed Loop · Part 2: Deliver the Right Thing to the Right Place
Pick Verification · Label Error-Proofing · Five Core Metrics
P.11
QTank · Quality Management Training Series
02 / 16

## Slide 3
01
CHAPTER · 01
Current State Insight
Invisible"Transport Fleet"
Many plants' quality management"Focuses on production lines but misses the shop floor transport fleet"——
Handling, storage, delivery, packaging, labeling — five linked links,
any failure voids all prior effort.
01
05
03 / 16

## Slide 4
01 · Current State Insight
Quality Department"Focuses on Production Line"，But Misses Shop Floor"Transport Fleet"
✓ Visible · Three Inspection Pillars
Incoming Inspection
Gate at the Door
In-Process Inspection
Guard at Process
Final Inspection
Watch Finished Goods
Every station has work instructions, first article confirmation, patrol checks —
Production Line Three Inspections"Visible", the quality department's main battlefield.
In-plant logistics is quality management's"Blind Spots"— managing production alone is insufficient; defense must extend to shop floor transport
✗ Invisible · Five Logistics Links
1
Handling
No Records
2
Storage
No Records
3
Delivery
No Records
4
Packaging
No Records
5
Labeling
No Records
No Inspection Data Generated
Yet Creates Quality Risk Daily
QTank · Quality Management Training Series
04 / 16

## Slide 5
02
CHAPTER · 02
Four"Quality Killers"
Before acting, know the enemy
Four most common in-plant logistics problems —
handling damage, wrong pick/delivery, mixed batch/broken traceability, storage degradation.
None visible to quality department until damage is done.
02
05
05 / 16

## Slide 6
02 · Four Quality Killers
Most Common in In-Plant LogisticsFour Problem Types, check against your shop floor
Common traits of all four:Occur where quality cannot see; damage done before exposure
①
Handling Damage
Transfer / Loading/Unloading
Impact Damage · Scratches · Deformation · Falls
Unpackaged stacking, over-height/overload bins
Forklift sharp turns, material falling from height
⚑ Highly Hidden
②
Wrong Pick/Delivery
Picking / Delivery
Similar materials stored adjacently
Picking relies on"Looks Like"
Delivery by experience to find station
⚑ Mix-up Follows
③
Broken Batch Traceability
Warehouse / Transfer
FIFO not enforced
Batch labels peeling or covered by oil
Traveler separated from physical item
⚑ Cannot Trace Batch
④
Storage Degradation
Warehouse / Racking
Temperature/humidity-sensitive material exposed
ESD components in regular plastic bags
Shelf-life materials overstocked and expired
⚑ Before Line Entry Already"Defective"
QTank · Quality Management Training Series
06 / 16

## Slide 7
03
CHAPTER · 03
Five-Step Framework
Manage Logistics as a Process Step
Handling, storage, delivery, packaging, labeling —
Five linked links; any failure voids prior effort.
Five steps are not pick-one — they areChained。
03
05
07 / 16

## Slide 8
03 · Five-Step System Overview
In-Plant Logistics Quality ControlComplete Closed Loop
Closed-loop core: Step 5 's"Measurement & Improvement"Feeds Back to Prior 4 Steps,
Quality Defense Line = Process Chain + Metric Feedback
Handling
HANDLING
Material Characteristic Matching
Container Standardization
1
Storage
STORAGE
Clear Separation · Easy to Find
First Out First
2
Delivery
DELIVERY
Pick Verification
On-Time Line Delivery
3
Packaging & Labeling
PACKAGE
Packaging Protection
Label Error-Proofing
4
Measurement Closed Loop
CLOSURE
5 KPI
PDCA Cycle
5
QTank · Quality Management Training Series
08 / 16

## Slide 9
04
CHAPTER · 04
Handling + Storage
Secure the First Two Gates
Handling Determines Product's"Initial State"，
Storage Determines Product's"Hold State"——
If first two gates fail, downstream three steps cannotRecover。
04
05
09 / 16

## Slide 10
STEP 01 · Handling Control
Make"Transport"Stop Creating Defects
Handling Scenario Illustration · Standardized Operations
Standardized Containers
Fixed Routes
Speed Limits 5km/h
Certified Operators
1
Match Handling Method to Material Characteristics
Precision Parts / Appearance parts use dedicated containers + Dividers and foam padding;ESD parts use ESD boxes;Liquids/powders use sealed containers. Match container to material type,Document in packaging specifications.
2
Standardize Transit Containers
Uniform specs, color, and load capacity for bins, racks, pallets;Physical limits for over-height/overload;Include damaged containers in daily checks.
3
Controlled Handling Routes and Speed
Fixed routes avoiding high-traffic areas;Slow down at turns, doorways, ramps;Fragile / Dedicated channels for fragile/precision materials + Speed limits.
4
Loading/Unloading Standards and Training
Standard actions for loading, unloading, shelving, line delivery;Handle with care — no throwing;Material handlers certified.
QTank · Quality Management Training Series
10 / 16

## Slide 11
STEP 02 · Storage Control
Make"Storage"Without Changing Product State
Storage Zoning · One Slot, One Material · Records-Cards-Physical Match
Conforming Zone
Quarantine Zone
Non-conforming
A · Conforming Zone
A01
A02
A03
A04
A05
A06
A07
A08
B · Quarantine Zone
B01
B02
B03
C · Non-conforming / Isolation
C01
C02
Clear Separation
By conforming/Quarantine/Non-conforming in separate zones;Similar materials in separate zones/racks;One slot one material, fixed locations.
Easy to Find
Records-Cards-Physical Match,Real-time inventory visibility;Complete batch registration — supplier/Production/Receiving/Inspection ID,All required.
First Out First
FIFO cannot rely on"Self-discipline",Needs systematic mechanism:AS/RS system enforcement + Flat warehouse color tags + Dual-location rotation,Visible and traceable.
Environmental Compliance
Temperature/humidity, cleanliness, ESD protection in specifications;Daily recording + Out-of-limit alerts;Shelf-life ledger + Expiry alerts and re-inspection.
QTank · Quality Management Training Series
11 / 16

## Slide 12
05
CHAPTER · 05
Delivery + Packaging + Closed Loop
Deliver the right material to the right station at the right time
Delivery is the interface between logistics and production,High-risk zone for wrong parts;
Packaging and labeling let products"Carry Identity"Flow;
Managed but Not Measured = Not Managed— Measurement and closed loop determine whether prior 4 steps sustain results.
05
05
12 / 16

## Slide 13
STEP 03 · Delivery Control
Deliver"the Right Material"at"the Right Time"to"the Right Station"
Three Delivery Essentials
1
Pick Verification
Pick list system-generated from work order,Item-by-item scan verification
Material barcode · Location code · Work order number Three-code match
Small plant fallback:One order, one cart, one label,Eliminate memory-based picking
Add verification step after picking,Item check and sign-off for release
2
On-Time Line Delivery
Early arrival blocks line-side space; late arrival stops line
Implement timed and quantified delivery,Fixed time windows
Back-calculate delivery frequency from production plan
Delivery Exceptions(Shortage/Wrong Part/Delay)Rapid response channel
3
Controlled Line-Side
Fixed line-side rack locations,One Slot, One Material
Verify batch and work order before line feed
Line clearance confirmation on changeover,All previous batch material removed
Inventory min/max — replenish low, alert high
Delivery Time Window · Exception Cases
✓ On-Time Arrival
✗ Early Arrival = Blocks Line-Side
✗ Late Arrival = Line Stop
Assessment
Delivery is not"just transport and done"——
Fixed time windows and rapid exception response,define controlled delivery.
Time Window
Occupies Space
Line Stop
QTank · Quality Management Training Series
13 / 16

## Slide 14
STEP 04 · Packaging & Labeling Control
Let products"Carry Identity"Flow
Three-Layer Packaging · End-to-End Labeling · Error-Proof Traceability
Three Key Points
1
Packaging Protection
Inner/Outer/Cushioning designed per product characteristics,Validated for drop, stack, and vibration.
Supplier packaging change / Re-validate when transport method changes.
Damaged packaging triggers separate inspection,Cannot go directly to line.
2
Complete Labeling
Each transit unit has unique identification:Material code + Batch number + Quantity + Date.
Labels travel with physical item,Peeling/Fading/Covered labels treated as anomaly,Re-label immediately and verify batch.
Prohibit"Unlabeled Material"from entering production line.
3
Label Error-Proofing
Use barcodes / QR codes / RFID instead of handwritten labels.
Unified label templates,Machine-printed batch information,Eliminate"Illegible handwritten batch numbers"。
Label integrity in daily logistics checks.
QTank · Quality Management Training Series
14 / 16

## Slide 15
STEP 05 · Measurement & Closed Loop
Logistics quality also needs"Accountability"
Wrong Part Count
0
times
Wrong pick/delivery in picking and delivery
Target = 0
FIFO Compliance Rate
≥ 95
%
Spot-check compliance,Below 95% Investigate mechanism
Baseline 95%
Traceability Success Rate
100
%
Random WIP sample,3 minutes to explain batch/Source/Status
Target 100%
Delivery On-Time Rate
100
%
Material arrives at line-side per time window
Target 100%
Damage Rate
≤ 0.5
%
Handling / Handling/storage damage count vs. total throughput
Baseline 0.5%
PDCA Closed-Loop Mechanism · Logistics Review
Detect
Metric Anomaly
Analyze
Root Cause Investigation
Countermeasure
System Improvement
Verify
Effect Tracking
Logistics Anomaly(Impact Damage / Wrong Part / Lost Labels)Same as Production Quality AnomalyEqual Treatment—— Analyze root cause, define countermeasures, verify effect;Monthly logistics review,Include in performance evaluation.
CLOSURE
"Managed but Not MeasuredEquals Not Managed"
Beyond Metrics,Need closed-loop mechanism —
Not"blaming handlers after incidents"
and moving on.
Logistics quality improvement follows
Detect—Analyze—Countermeasure—Verify cycle.
QTank · Quality Management Training Series
15 / 16

## Slide 16
Thank You
qtank.org
QTank
qtank.org